## Slide 2
Methodology of assembly:
Add a row of permanent magnets.
Stack up laminations.

## Slide 3
Assembly fixture used
Double acting air cylinders
Mechanically actuated hitch pin

## Slide 5
Arrows indicate potential lamination stack weld areas to reduce stack shearing movement.
Add hydraulics to improve stack density.

## Slide 6
Magnet backleg assembly should be assembled, adjusted, and pinned before addition of permanent magnets and poles.

## Slide 7
Worst problem encountered was the inconsistencies in size of aluminum spacers.
Use of permanent magnet jacking screws.
Re-measuring all components prior to assembly is essential.
Remediation
Issue

## Slide 8
Ordered non magnetic tools.
Tightening these screws problematic.
Remediation
Issue