## Slide 1
Overview
  Carbon fiber composites have been used for a long time but sparsely for structural applications due to brittleness
  Thermoplastic carbon composites are more promising as they have a higher stiffness to weight ratio and provide a more crystalline structure than epoxy cured composites
  The crystalline structure of the thermoplastic allows X-ray diffraction techniques to more accurately measure the stress and strain states within the composites
Design of Test Fixture for X-ray Diffraction Measurement of Thermoplastic Carbon Composites in Bending at MSN-C
By: Ian Hahn
Mentors: Arthur Woll, Armand Beaudoin
Guidance from: Joe Crum, Basil Blank
Figure 1: Four-point bending diagram with shear and moment diagrams
Design Process
  Refamiliarize with 4-point bending
    Pure bending
    Clear strain profile
  ASTM 7264 – Standard for testing flexural properties of polymer composites
    Provided aspect ratio
  Discussions with other scientists helped to set specimen and fixture dimensions

## Slide 2
Design of Test Fixture for X-ray Diffraction Measurement of Thermoplastic Carbon Composites in Bending at MSN-C
Practical Considerations
  Alignment of top and bottom housing with pillow blocks and linear bearings
  Addition of c-flex bearing to accommodate for specimen imperfections
  Reconfiguration of the support and load spans to accommodate different bending configurations as well as varying span dimensions
  100 lb. in-line compression load cell

## Slide 3
Design of Test Fixture for X-ray Diffraction Measurement of Thermoplastic Carbon Composites in Bending at MSN-C
Deflection Calculations
  Maximum deflection at beam center
    .75 mm
  Deflection at load points
    .50 mm
  Using M4 x 0.7 load screw
    Load point deflection correlates to 257 degree turn of screw
  E – Elastic modulus
  I – Moment of inertia of the cross-section of the specimen