## Slide 1: Effects of reflections on TE-wave measurements of electron cloud density
Kenneth Hammond
Mentors: John Sikora and Kiran Sonnad

## Slide 2: Overview
Need to measure electron cloud (EC) density
TE-wave transmission method
  Wave transmitted and received by BPM buttons
  EC acts as a dielectric
  Modulations in EC affect wave speed and thus the phase at the receiver

## Slide 3: Overview
Determines spatial average EC density
Data interpretation
  Fourier transform of transmitted wave is analyzed
  Modulations in phase appear as frequency sidebands

## Slide 4: Overview
Challenges
  Irregular beam pipe geometry
    Cross-section makes theoretical modeling difficult
    Numerical simulation is necessary
  Amplitude modulation
    Can occur in the presence of constant magnetic fields
  Reflections
    Primarily due to changes in cross-sectional geometry
    Can greatly affect average phase advance

## Slide 5: Overview
Tasks
  Use physical waveguide to confirm accuracy of simulation
  Simulate beam pipe with CESR geometry
  Measure changes in phase advance brought about by changes EC density and reflections

## Slide 6: The Physics of Waveguides
Resonance
  In practice, reflection will occur
    Waveguide exhibits properties of a resonant cavity
  Standing waves form at wavelengths harmonic with waveguide length

## Slide 7: The Physics of Waveguides
f 2 = an2 + b2
a = (c/2L)2
b = fc

## Slide 8: The Physics of Waveguides
Phase advance and ΔΦ
  Dispersion relation:
  Phase velocity:
  Phase advance:
  “Phase shift”:

## Slide 9: Simulation
VORPAL software models waveguide system numerically
Input boundary conditions
  Conductor walls
  Transmitting antenna
Solve Maxwell’s Equations

## Slide 10: Simulation
Special features
  Grid boundaries
    Automatically ascribes perfect-conductor boundary conditions to specified surfaces
    Cubic cells may be “cut” diagonally

## Slide 11: Simulation
Special features
  Particles
    Distribution can be controlled
    Simulation accounts for positions, velocities, and forces

## Slide 12: Simulation
Special features
  PML (perfectly matched layer) boundaries
    Absorb all incident waves
    Allows simulation of a segment of an infinite pipe with no reflections

## Slide 13: Simulation
Differences with physical measurements
  Time scale
    Most simulations modeled the system for 70ns
    Longer simulations exhibit roundoff error
    Frequency sweeps are not practical

## Slide 14: Experiments
#1: Phase shifts without reflection
  Multiple trials at different electron densities
PML
PML
ρ
measure voltage

## Slide 15: Results
#1: Phase shifts without reflection

## Slide 16: Experiments
#2: Phase shifts with reflection
  Add conducting protrusions
  Transmit waves at resonant frequencies to maximize reflection
PML
PML
ρ
measure voltage

## Slide 17: Results
#2: Phase shifts with reflection

## Slide 18: Results
Physical evidence in support of inconsistent phase shifts
  Transmission through a plastic dielectric

## Slide 19: Results

## Slide 20: So, what next?
Simulate phase shifts at more frequencies
Streamline the method for extracting phase shift
Study phase shifts for different electron cloud distributions

## Slide 21: Acknowledgments
Special thanks to
John Sikora
Kiran Sonnad
Seth Veitzer

## Slide 22: Effects of reflections on TE-wave measurements of electron cloud density
Kenneth Hammond
Mentors: John Sikora and Kiran Sonnad

## Slide 23: Simulation
Differences with physical measurements
  Transfer function
    A 70ns signal is essentially a square pulse
carrier frequency

## Slide 24: Experiments
Calculating ΔΦ
  Record voltage over time for two simulations
  Normalize voltage functions
  Subtract one set of data from the other

## Slide 25: Physical model
Pipe length: l = 1.219m
Flange walls: l = 1.329m
Optimized length: 1.281m

## Slide 26: Physical model

## Slide 27: Physical model

## Slide 28: Physical model

## Slide 29: Physical model

## Slide 30: Physical model

## Slide 31: Physical model

## Slide 32: Physical model

## Slide 33: Physical model

## Slide 34: Physical model
Rectangular copper pipe

## Slide 35: The Physics of Waveguides
Waveguide: a hollow metal pipe
Facilitates efficient RF energy transfer
Cutoff frequency: minimum frequency required for transmission
  Determined by cross-sectional geometry