## Slide 1: Modeling LCLS, LCLS-II:
Christopher Mayes
October 30, 2017
Bmad and Beyond

## Slide 2: Bmad Overview
Written in Fortran 2008.
Object-oriented from the ground up.
Has structure translation code for interfacing with C++.
With certain restrictions, Bmad can be run multi-threaded.
Lattice files use a MAD like syntax.
Well documented (Manual is ~500 pages).
  Open Source: http://www.lepp.cornell.edu/~dcs/bmad/
type (lat_struct) lat
call bmad_parser (‘lat.bmad’, lat)
Notes: In this example lat is an instance of a lat_struct.
A lat_struct is a structure that holds all the information about a lattice.
Including a list of the lattice elements, magnet strengths, etc.
The call to bmad_parser takes a lattice file name
and bmad_parser will fill the lat instance with the parsed information

## Slide 3: In the Beginning…
Brief History of Bmad:
  Bmad is a software toolkit for the simulation of charged particles and X-rays.
  Born at Cornell in mid 1990s
  Started life as modest project: Just wanted to calculate Twiss functions and closed orbits.
  Initially Bmad used a subset of the MAD lattice syntax. Hence the name: “Baby MAD” or “Bmad” for short.
Over the years Bmad had evolved…
Notes: And Baby has grown up

## Slide 4: And Baby Grows Up...
Currently:
    ~100,000 lines of code
    ~1,000 routines
And it can do much more:
    Lattice design
    X-ray simulations
    Spin tracking
    Wakefields and HOMs
    Beam breakup simulations in ERLs
    Intra-beam scattering (IBS) simulations
    Coherent Synchrotron Radiation (CSR)
    Touschek Simulations
    Frequency map analysis
    Dark current tracking
    Etc., etc.

## Slide 5: Bmad Philosophy
Advantages of a toolkit:
  Cuts down on the time needed to develop programs.
  Cuts down on programming errors (via code reuse).
  Provides a simple mechanism for lattice function calculations from within control system programs.
  Standardizes sharing of lattice information between programs.
Bmad
Dynamic Aperture Program
Control System Programs
Lattice Design Program
Etc.
IBS Simulation Programs

## Slide 6: Superposition
Physical Layout:
Internal lat_struct Representation:
Lords:
Tracking
elements:
Superposition allows element overlap. In the lattice file:
  cesr: line = (... q1e, dft, ip, dft, q1w ...)
  cleo: solenoid, l = 3.5, superimpose, ref = ip
And Bmad does the bookkeeping…
Simplifies life for both user and programmer:
  Simplifies lattice file construction
  Simplifies varying element attributes in a program

## Slide 7: Forking
to_LER: fork, to_line = ler, to_element = injection
inj: line = (..., to_LER) ! injection line
LER: line = (..., injection, ...) ! LER ring
use, inj
Bmad can join different beam lines using fork elements.
Example: SuperKEKB Low Energy Ring (LER) injection
Can splice together rings, dump lines, Linacs, X-ray lines, etc.  One lattice can hold the description of the entire accelerator complex.

## Slide 8: Multipass
Lines having common elements. Example ERL loop:
BEND_L1: sbend, angle = -25*pi/180, l = 0.2, ...
BEND_L2: BEND_L1
A_PATCH: patch, flexible = T
D_PATCH: patch, x_offset = -0.034, x_offset = asin(-0.32)
INJECT: line = (...)
LINAC: line[multipass] = (BEND_L1, ..., BEND_L2)
ARC: line = (..., BEND_A7)
DUMP: line = (...)
ERL: line = (INJECT, LINAC, ARC, A_PATCH, LINAC, D_PATCH, DUMP)

## Slide 9: Tracking method selection
  bmad_standard Fast, nonsymplectic
  symp_lie_ptc Symplectic tracking using PTC
  taylor Taylor map tracking using PTC
  linear Linear tracking
  runge_kutta Track through fields.
  custom Tracking with custom code
  …
Can set how each element is tracked:
Advantages:
  Enables simulation of unique element types
  Can compare different tracking methods
my_ele: em_field, tracking_method = runge_kutta, field_calc=custom, ...

## Slide 10: All elements and tracking methods
Spin

## Slide 11: Etienne Forest’s FPP/PTC
Interface routines between Bmad and PTC allow tracking of individual elements or PTC lattices can be constructed for analysis.
Etienne Forest’s FPP/PTC simulation toolkit:
  Taylor maps to arbitrary order via symplectic integration through elements.
  Spin tracking.
  Normal form analysis.
  Amplitude Dependent Spin Tune and Invariant Spin Field calculations.
  Also used in MAD-X & PTC_ORBIT
FFAG cell
One turn map calc in Tao

## Slide 12: X-ray simulation
Bragg crystal diffraction simulation
Both incoherent and coherent ray-tracing implemented (but needs more testing).
X-ray tracking elements developed:
  Crystal ! Bragg & Laue diffraction
  Capillary ! Focus X-rays
  Mirror
  Multilayer Mirror
  Diffraction_plate ! Apertures, Zone plates

## Slide 13: CSR with Shielding
We developed and benchmarked a 1-D CSR simulation technique with shielding by the vacuum chamber in Bmad
[Sagan, Hoffstaetter, Mayes, Sae-Ueng PRST-AB 12, 040703 (2009)]
Compared with Agoh & Yokoya
Exit Transient
shielding
Free space

## Slide 14: Transverse Space Charge
1 nC bunch through straight FFAG section at 42 MeV
Also in the 2009 paper was an excellent approximation of the space charge kick due to a Gaussian slice
This includes both longitudinal and transverse space charge

## Slide 15: Longitudinal Space Charge
Also in the 2009 paper was an excellent approximation of the space charge kick due to a Gaussian slice
This includes both longitudinal and transverse space charge
Bmad
GPT

## Slide 16: More general 1-D CSR model
Page Headline
Beam follows reference (bends with quad moment)
Beam orbit with offset quads
The old code and 2009 paper assumed that the beam followed the reference coordinate system
The new code has been generalized to deal with arbitrary orbit.
IPAC17:THPAB076

## Slide 17: NEW: 3D spacecharge
Page Headline
Robert Ryne (LBNL, original author of IMPACT) has developed a new stand-alone space charge package.
Parallelized via MPI
Open source
New collaboration to generalize its use for easy integration into other codes.
Currently incorporating it into Bmad
Adding OpenMP parallelization.
Benchmarks well with Astra, ImpactZ, MaryLie/IMPACT

## Slide 18: Bmad Ecosystem
Due to its flexibility, Bmad has been used in a number of programs including:
  tao General purpose design and simulation.
  synrad3d 3D tracking of synch photons, including reflections, within the beam chamber.
  cesrv On-line data taking, simulation, and machine correction for CESR.
  dark_current_tracker Dark current electron simulation.
  freq_map Frequency map analysis.
  ibs_sim Analytic intra-beam scattering (IBS) calculation.
  touschek_track Tracking of Touschek particles.
  etc...
  Code reuse: Modules developed for one program can, via Bmad, be used in other programs.

## Slide 19: Dark Current Tracking for LCLS2
Field emitters
https://www.classe.cornell.edu/~cem52/LCLS2/2015_09_16-LCLS2_dark_current.pdf

## Slide 20: Tao: Tool for Accelerator Optics
Problem: Bmad is not a program so it cannot be used “out of the box” for simple calculations.
Solution: Develop Tao - a general purpose simulation & design program with
  Twiss and orbit calculations.
  Nonlinear optimization.
  Analysis of complicated geometries.
  Etc.
Additionally: Tao’s object oriented coding makes it relatively easy to extend it.
  Can add custom commands to interface Tao with a control system.
  Can be driven by Python
CBETA 4-pass ERL

## Slide 21: Tao [continued]
Tao with Bmad gives the flexibility of a library with the convenience of a program.
Example: Designing or modifying a machine to be/stay within an existing building:

## Slide 22: Tao running the LCLS2 lattice

## Slide 23: Tao as an online model
Python >>>
>>> from pytao.tao import Tao
>>> tao = Tao('-lat my_lat.bmad')
>>> tao.command('use var *')
>>> doutput = tao.capture('show top10')
>>> print(output)
Python wrapper
Tao> call read_EPICS.tao
(repeat)
Tao> call write_data.tao
Tao Live interactive display
CSR, Space Charge tracking
Tao> use data bpms
Tao> use variable quad_offsets
Tao> derivative. ! Calculates response of offset quad to BPM
Tao> show derivative
Tao> call read_BPMS_EPICS.tao
Tao> run_optimizer
Discover errors

## Slide 24: Bmad online model of LCLS (Current State)
Tao> call scripts/live_update.tao
Design lattice in:
/u/ad/cmayes/LCLS/model
Complete translation of the MAD lattice, including comments and structure
Overlays to add functionally for:
  Klystrons [ENLD, PHAS, STAT], including feedback klystrons
  Bunch compressors [angle]
  Linac overall [phase, fudge]
Python scripts read EPICS PV values, write Bmad compatible statements
Tao script for ‘LEMing’ based on energy measurement PVs
October 30, 7 pm

## Slide 25: Summary Bmad advantages
  State-of-the-art tracking methods, fast and slow
  Arbitrary trajectory 1-D CSR model with shielding
  Medium-High energy space charge model
  New: 3D Space Charge
  Field maps for any element, can overlap other elements
  Superposition: Greatly simplifies lattice layout, bookkeeping
  Patch element: Enables arbitrary arrangement of magnets
  Controller elements: define arbitrary knobs
  Continuous beam chamber walls, masks
  Forking: Multiple connected lines
  Reads MAD, XSIF, SAD lattice formats
  Translation routines to Astra, OPAL, MAD, XSIF, SAD, …
  Spin tracking
  X-ray tracking
  Dark current tracking
  Software toolkit: Maximum flexibility for custom programs

## Slide 26: Summary Tao advantages
  Design tool
  Fast online optics calculation
  Multiple optimization methods
  Bunch tracking with CSR, Space charge
  Response of anything to anything: effect of quad misalignments, etc.
  Wave analysis: discover isolated orbit and focusing errors.
  Built-in plotting
  Customizable via hook routines, e.g. interface with a control system
  Python interface for automation, advanced GUIs, also interface with control systems

## Slide 27: SLAC FEL Lightsource Modeling
Goals:
  Maximize FEL performance.
  Minimize downtime (rapid/automated tuneup, diagnose problems).
  Enable advanced beam dynamics studies.
Existing modeling problems:
  LCLS: Measured optics do not match existing model, no collective effects
  LCLS-II: Collective effects and their impact on FEL performance are not fully understood
  LCLS-II-HE: Space charge limits the injected emittance; What bunch qualities are really needed at injection?

## Slide 28: Current state of modeling
Astra
ImpactZ
Genesis
elegant
?
electron/photon divide
ImpactT
MAD description
Simulation codes
SLAC Matlab MAD
SLAC MAD8

## Slide 29: SLAC FEL Lightsource Modeling
Proposal:
Construct realistic start-to-end models of the electron machines (LCLS, LCLS-II, LCLS-II-HE).
Develop a simulation pipeline for tracking electrons from the cathode through X-ray production.
Bridge this to X-ray transport simulation pipeline.

## Slide 30: Benefits
A realistic start-to-end model and simulation framework will enable holistic optimization, understanding, and performance prediction of SLAC’s lightsources.
For the existing machines (LCLS, soon LCLS-II), this would be used as an operational tool to understand and tune-up the machine.
For future machines (LCLS-II-HE and beyond) it would be used to understand requirements for various components (e.g. electron gun, injector) and sensitivities.
Subtle beam physics effects that limit ultimate performance would be identified early on.
When bridged with X-ray transport, this would be used to predict the success of individualized experiments.
The model could be optimized as a whole (correlate experiment performance with accelerator parameters), or be used to train machine learning algorithms for online control.

## Slide 31: Plan
Most of the simulation codes and techniques exist, but are not bridged. We will:
Identify the relevant codes and human expertise for each of the parts of the machine (injector, Linac, beam transport, FEL light production, X-ray optics, X-ray final focus, detector)
  Avoid re-inventing the wheel: Use existing, well-developed codes as much as possible (e.g. Impact, Bmad, Genesis)
Quantify and experimentally validate various beam effects (e.g. space charge, coherent synchrotron radiation, wakefields)
Tune models to match machine measurements (e.g. alignment, field errors)
Develop a software wrapper to enable ‘push button’ start-to-end simulation runs usable by both experts and students.
Collaborate with the X-ray optics group (which is pursuing a parallel effort) for truly start-to-end simulations.

## Slide 32: Future: LCLS-I, LCLS-II, LCLS-II-HE, …
Simulation tools
Custom simulation pipeline
Start-to-End simulation