First Look at the New SYNRAD3D Results
-- Comparison with previous simple vacuum chamber wall model (9x5 cm elliptical)–
-- Comparison of new simple wall calculation with new detailed wall model --
Lots of work by Takuya Ishibashi, Gerry Dugan, David Sagan and Sergey Milashuk
Jim Crittenden
Cornell Laboratory for Accelerator-Based Sciences and Education
Electron Cloud Meeting
15 June 2011

---
 Compare old and new with smooth wall file
5.3 GeV e+, 15W (TiN) Shielded Pickup
Old SYNRAD3d with smooth wall file
New SYNRAD3d with smooth wall file
Similar results for the number of reflections prior to absorption.

---
5.3 GeV e+, 15W (TiN) Shielded Pickup
Old SYNRAD3d with smooth wall file
While the total reflectivity has changed little, the azimuthal distribution of absorbed photons is quite different.
This will have significant consequences for the ECLOUD simulation of the SPU signal.
How has SYNRAD3D changed?

---
5.3 GeV e+, 5 mA/bunch, 15W (TiN) Shielded Pickup
Old SYNRAD3d with smooth wall file
Comparing witness bunch simulations without tuning the ECLOUD input parameters
The witness bunch simulations have been much improved by introducing more flexible photoelectron energy distributions
and tuning other input parameters such as the secondary energy distribution. In particular, the introduction of independent p.e. energy distributions and quantum efficiencies for direct and reflected photons will serve to adapt to the new SYNRAD3D calculations. The above comparison points to increasing the quantum efficiency for reflected photons.

---
 Compare new smooth and realistic wall files
5.3 GeV e+, 15W Shielded Pickup
New SYNRAD3d with realistic wall file
Significantly fewer reflections with the realistic wall file.

---
5.3 GeV e+, 15W (TiN) Shielded Pickup
New SYNRAD3d with realistic wall file
The new realistic wall file predicts dramatically less (factor < 0.5) reflected photoelectrons from scattered photons
and that they will come primarily from the inside wall of the beampipe. The SPU measurements can be expected to
provide stringent tests of these predictions.

---
5.3 GeV e+, 5 mA/bunch, 15W (TiN) Shielded Pickup
New SYNRAD3d with realistic wall file
The SYNRAD3D calculation using the detailed wall file indicates almost no SPU signal from the bottom of the beampipe. Since we do see such a signal, we need to investigate the SYNRAD3D calculation in detail to understand the origin and credibility of its prediction.