Coherent Tune Shift Measurements
in CHESS Arc Pretzel Conditions
Jim Crittenden, Stephen Poprocki, John San Soucie
Machine Studies Meeting
16 June 2015

---
Coherent tune shifts from field gradients
5.289 GeV 45 e+ bunches
1.0 mA/bunch
0.5 mA/bunch
4.0 mA/bunch
2.0 mA/bunch
Tune shifts calculated from horizontal and vertical electric field gradients at the center of the beam pipe.
Longitudinal time-slice charge-weighted average is uses the six time slices per bunch.
Lots of information here. Simulation will be challenging.

---
Measurement and ECLOUD modeling for Feb/2009 tune shift measurements with 45-bunch 2.1 GeV positron trains
(Slide 4 of talk on 11 Nov 2009)
0.8 mA/bunch
0.4 mA/bunch
Remarkably successful modeling of vertical tune shift along 45-bunch positron trains showing the relative contributions of the drift (23%) and dipole (62%) regions.
By the way, one point in this talk was that there was a significant dependence of the model on the vertical beam size, the tune shifts increasing for larger beam size.
0.4 mA/bunch

---
Pinch effect
Transverse cloud charge distributions for 11 time slices during bunch 20 in a 2 mm x 2 mm area
Drift region
800 G dipole field

---
Gaussian + flat background fits to the pinched cloud in bunch 20 for the 800-G dipole
Horizontal
Vertical

---
Beam-weighted cloud densities for bunches 11-20
4e12/m3
1e12/m3
4e12/m3
2e12/m3
We don't yet know which cloud characteristic will describe the emittance blowup.
If the density averaged over the beam region varying along the bunch length is important,
a dependence on train length would indicate the relative contribution of the drift regions.

---
Effect of quadrupling the bunch current
for the 800-G dipole case
1.2e10 e+/bunch
4.8e10 e+/bunch