Title
Progress in ECLOUD Simulations for the 5.3 GeV e+ Witness Bunch Measurements
with the Shielded Pickups
Ryan Badman
 Jim Crittenden
July 20, 2011
Electron Cloud Meeting

---
Improvements and End Result
-As mentioned by Jim Crittenden at the 7/13 meeting, the witness
bunch simulations have been improved by independently adjusting
quantum efficiencies and energy distributions for direct and
reflected photons, and tuning other input parameters
such as the secondary energy distribution.
-The secondary energy distribution
will be the focus of this talk,
both the functional form and
the input parameter SEMAX.
Present status of optimization

---
Intro to Changes in Secondary Energy Distribution
ECLOUD simulations up to now have used the distributions introduced by Noel Hilleret based on Phil.J.Res. 50 (1996), 375:
f(Esec) ~ exp( -ln(Esec/SEMAX)2/2 ), with SEMAX=1.8 eV
Use of a distribution attributed to Miguel Furman improved the comparison to data:
f(Esec) ~ Esec exp (-Esec/SEMAX ), with SEMAX=0.8 eV
As the next two slides will show, Noel's distribution has too many high energy e-, giving a broad late signal after the leading bunch
which is not seen in the measurements.
Original
Optimized
Original
Optimized

---
      Original vs. Optimized
f(Esec) ~ Esec exp (-Esec/SEMAX )
SEMAX=0.8 eV
f(Esec) ~ exp( -ln(Esec/SEMAX)2/2 )
SEMAX=1.8 eV

---
Why Miguel's Distribution is Used
When the same optimal value of 0.8 eV is used for both, the exponential functional form eliminates the nonphysical late broad peak observed with the original ECLOUD parabolic log function.
Parabolic log (Noel)
Exponential (Miguel)
eV

---
        peak
        not in
        data
Sensitivity to SEMAX Parameter (Miguel's function)
(Note the late simulation peak at SEMAX>0.8 eV that is not present in the data)

---
Where does late peak come from?
Photoelectrons from the top of the beam pipe and from direct photons produce
secondaries that cause this signal.

---
Lower bound on SEMAX obtained from 14-ns witness bunch signal shape

---
Summary
1) 5.3 GeV simulations have made great progress in describing the SPU witness bunch data.
2) The best SEMAX value is around 0.8 eV. Above 1.0 eV an unphysical, late, broad peak appears in the simulation. Below 0.8 eV, the 14-ns witness bunch signal shape simulation is poor.
3) The senstitivity to SEMAX appears to be about 0.2 eV.
4) Miguel's exponential distribution gives a better match than the Phil.J.Res. parabolic log function.
5) Future work: Will the 2.1 GeV analysis corroborate this result for the 5.3 GeV data?