New Plotting Tools
ECLOUD spacecharge field
(Example: Trapped cloud space charge field)
Synrad3D output analysis
(Example: RFA 40E1 SEY station after L3 vacuum chamber correction)
-- Updated Synrad3D plots on 3/4/2014. Added comparison to Synrad3D analysis of Jan/2012 --
Jim Crittenden
Electron Cloud Meeting
26 February 2014

---
ECLOUD quad trapping model
Central spacecharge field values
Averaged over entire 2.7 ms of simulation
Snapshot at end of turn
Spacecharge field written prior and during each beam bunch (15 slices). Field values are small.

---
2D time-averaged field profile
over full 4.8-cm-radius circular vacuum chamber
Hot spots in horizontal plane

---
2D spacecharge field profile
over +- 2.4 cm
Snapshot at end of turn
The trapped field is about 1/10 V/m.

---
2D spacecharge field profile
over +- 2.4 cm
Snapshot at end of turn
The trapped field is about 1/10 V/m.

---
Synrad3D Output for RFA 49E1 (SEY station)
CHESS lattice – 5k photons
Positron beam
(0.04 g/m/e+, 8 hrs run time)
Electron beam
(0.30 g/m/e-, 1 hr run time)
B48W
B48E
L3 vacuum chamber corrected for these runs. Now 3.5 inch (8.9 cm) diameter throughout.

---
Synrad3D Output for RFA 49E1 (SEY station)
CHESS lattice – 5k photons
Positron beam
Electron beam
Average absorbed photon energy falls rapidly with the number of reflections.

---
Synrad3D Output for RFA 49E1 (SEY station)
CHESS lattice – 5k photons
Synrad3D Jan/12
5.5 cm radius v.c. in L3
Synrad3D Feb/14
4.45 cm radius v.c. in L3
Positron beam
Electron beam
The vacuum chamber radius has been reduced from 5.5 cm to 4.45 cm between Q48W and Q48E,
removing a nearby mask at 49E1 for the light from the electron beam.
Now there is more direct light from both beams, but it is only a relatively small contribution to the overall rate.