Fields resulting from geometry errors in the newly assembled and installed EC quad magnet at 15W
Jim Crittenden and John Sikora
Electron Cloud/Impedance Meeting
28 September 2016

---
Central Field Uniformity
1 / 16 → 1 / 2 Model
PAC2005 Q03W Fast Lumi Quad
2016 EC Detector Quad at 15W
Specification is the deviation of the field from linear, rather than the gradient itself.
The additional numerical fluctuations in the ½ model are well within specification, but the calculations are now about 10 hours per model .

---
Measured Geometrical Errors
1) SW-NE diagonal bore error of 0.38 mm. 2) Lower aisle quadrant short by 1.6 mm.
With Errors
The bore error alone affects the central field uniformity. It lowers the gradient by 2.5 per mil with negligible consequence for the L/R symmetry.

---
Field Integral Uniformity
1 / 16 → 1 / 2 Model
PAC2005 Q03W Fast Lumi Quad
The additional numerical fluctuations in the ½ model are well within specification.

---
Measured Geometrical Errors
1) SW-NE diagonal bore error of 0.38 mm. 2) Lower aisle quadrant short by 1.6 mm.
With Errors
Both errors contribute to the field integral uniformity. Any field asymmetry introduced is negligible.