Quad Shielded Pickup (QSPU) Measurement
January 3, 2014
John Sikora

---
Quad SPU
Shielded Pickup installed in Q48W at CesrTA
The collector is centered on the quad pole face and centered longitudinally
(Another collector is in the fringe field of the quadrupole.)
300 holes of 1/32 inch allow the electrons to pass from the beam-pipe onto the collectors.
The 5.3 GeV positron data that follows was taken on December 23, 2013.
All witness bunches are 8 mA/bunch.

---
20-Bunch Data
20-Bunch Data versus Bunch Current
The collector signal increases rapidly with bunch current
The 8 mA/bunch signal changed between the start and the end of the experiment.

---
 1-Bunch, 6-Bunch and 9x1 Data
Data without the 20-Bunch Train
Data with 1-bunch and 6-bunch trains as well as 9x1 ~evenly spaced (left) were taken without the 20-bunch train for reference. The bunch current was 8 mA.
On an expanded scale, 1-bunch data and 9x1 data (right) are not the same (right). Arrows show the times of the 9x1 bunches. Do each of the 9x1 bunches leave electrons trapped in the quadrupole?

---
With a Single Witness Bunch
20-Bunch Train with Single Witness Bunches
With single 8 mA witness bunches after a 20-bunch train, the single bunch signals are significantly larger than they were without the train (as seen on the previous slide).

---
With a Witness Train
20-Bunch Train with a 6-Bunch Witness Train
With a 8 mA/bunch 6-bunch witness train after a 20-bunch train, the witness signals are significantly larger than they were without the 20-bunch train (which was about 15 mV as seen on slide 4).

---
.
Summary and Comments
The difference between data taken with and without the 20-bunch train clearly shows that the 20-bunch train leaves trapped cloud behind.
The 20-bunch train signal changed between the beginning and the end of the experiment. Why?
1-bunch and 9x1 bunch data are different. Is this due to direct beam signal, instrumentation problems, or cloud left behind by each of the 9 bunches?