ECLOUD Calculations of Coherent Tune Shifts
in Dipole and Quadrupole Fields Over Many Turns
 Followup to talks of 9 and 16 Dec 2009
8 March 2010: Corrected slide reference on slide 2
Jim Crittenden
Cornell Laboratory for Accelerator-Based Sciences and Education
Electron Cloud Meeting
3 March 2010

---
Slide 5 of talk on 9 December 2010
Quadrupole tune shift contribution assuming dipole ring averages
June, 2008 vertical tune shift measurements
Data from Fig. 2 of
PAC2009 FR5RFP044
5.3 GeV, 0.75 mA/bunch
Dipole (0.2 T)
Quadrupole (9.2 T/m)
Drift + Dipole
Drift+Quadrupole
Dipole
Drift
Drift
Quadrupole
The assumption of dipole ring averages (61.5% occupancy and 1.16 photons/m/e) exaggerates
the quadrupole contribution (8.5%, 0.78 photons/m/e) by more than a factor of 10.
The quadrupole contribution thus calculated is nonetheless only about 20% of the dipole contribution
during the passage of the filled bunches. It can be neglected at the 2% level.

---
But does the quadrupole contribution
accumulate over many turns?
Not for 11-bunch trains.
What about for 45-bunch trains, where secondary emission dominates?

---
Does the quadrupole contribution accumulate
over many turns for 45-bunch trains?
The cumulative effect slows after about six turns. Here only 45 of 183 bunches are filled.
NB: A circular beam pipe would reduce the average secondary yield.

---
Field Gradients at the Center of the Vacuum Chamber
The tune shifts calculated from the field gradients at the center of the vacuum chamber show turn-to-turn buildup behavior similar to that for those calculated with offset beams.
Again conclude that the quadrupole contribution can be neglected at the level of a few percent.