Comparison of old SYNRAD3D using the smooth elliptical wall file and the new SYNRAD3D including diffuse scattering using the realistic wall file
Diffuse scattering calculated for wall roughness 100 nm and correlation length 5000 nm
-- Witness bunch studies at 15E and 15W --
-- Coherent tune shift measurement/simulation comparison as published at IPAC10 –
6 January 2012: Updated plots with full azimuthal range and added drift/dipole distributions.
Jim Crittenden
Cornell Laboratory for Accelerator-Based Sciences and Education
Electron Cloud Meeting
4 January 2012

---
15E/W Geometry and SYNRAD/SYNRAD3D Comparison
Slide from talk of 8 September 2010
15W
15E
SYNRAD and SYNRAD3D calculate a similar e-/e+ direct rate ratio at 15E and 15W, but SYNRAD3D rates are lower
because more than half the direct photons are reflected.
SYNRAD3D also shows the degree to which the ring symmetry reverses the reflectivity.

---
 Compare old SYNRAD3d with smooth wall file and
new code with realistic wall file including diffuse scattering
chess_20090225, 5.3 GeV e+, 15W Shielded Pickup
Old SYNRAD3d with smooth wall file
New SYNRAD3d including diffuse scattering
 with realistic wall file
Assuming
QE = 24%
Top
Bottom
ECLOUD simulations to date have been done for p.e. rates on the bottom of the beampipe of about 0.003 pe/m/e.
With the smooth wall file, the rates at the top and bottom of the beampipe are due to the (unrealistic) elliptical shape of the vacuum chamber at the outside wall. With the realistic wall file, the rates are due to the diffuse scattering component.

---
 Shielded Pickup Witness Bunch Study
5.3 GeV e+, 5 mA/bunch, 15W (TiN) Shielded Pickup
New SYNRAD3d with realistic wall file
Comparing witness bunch simulations with no further tuning of ECLOUD input parameters
The comparison with the data is similarly satisfactory, even though the distribution of photoelectrons produced by scattered photons is substantially different.

---
 Compare old SYNRAD3d with smooth wall file and
new code with realistic wall file including diffuse scattering
chess_20090225, 5.3 GeV e+, 15E Shielded Pickup
Assuming
QE = 27%
In contrast to 15W, both the old and new SYNRAD3d calculations give high rates of photons incident on the inner wall.
(Reminder: my talk of 24Nov11 showed the rate on the inner wall to be important to match the SPU signal shapes.)
The distributions of photons on the top and bottom of the beampipe are quite different.

---
5.3 GeV e+, 3 mA/bunch, 15E (Carbon) Shielded Pickup
New SYNRAD3d with realistic wall file
Comparing witness bunch simulations without tuning the ECLOUD input parameters
Again, the new SYNRAD3d calculations provide a good description of the data.

---
 Compare old SYNRAD3d with smooth wall file and
new code with realistic wall file including diffuse scattering
2085mev_20090516, 2.1 GeV e+, ring-wide drift and dipole averages
Assuming
QE = 10%
Field-free regions
Dipole regions
The diffuse scattering with vertical vacuum chamber sides results in an 76% higher photon rate in the drift regions and 21% lower rate in the dipole regions. The azimuthal distribution is now much more similar in drift and dipole regions.

---
 IPAC10 & Phase 1 Report Tune Shift Measurements
1 February 2009 2.1 GeV 45-bunch train e+
0.4 mA/bunch
0.8 mA/bunch
The ECLOUD calculations using SYNRAD (no photon scattering, refl=15%) published at IPAC10 have been repeated using the old and new SYNRAD3D results without tuning of any other input parameters.
In both cases the drift contribution to the tune shift increases significantly, more so with the realistic wall and diffuse scattering.
The match to the data is about as good. The match to the new SYNRAD3D would improve with a trivial 5% reduction in QE.

---
 IPAC10 & Phase 1 Report Tune Shift Measurements
1 February 2009 2.1 GeV 45-bunch train e+
IPAC10 Results
SYNRAD (no photon scattering, refl=15%)
0.4 mA/bunch
0.8 mA/bunch
These comparisons substantiate the claims made on the previous slide concerning the consequences of photon scattering calculations for the modeling of coherent tune shift measurements. The IPAC10 results required extensive tuning, including the introduction of the rediffused SEY component and statistical approximations such as electrostatic grid size.
With no further tuning, the SYNRAD3d photon scattering model gives a good match, with dramatically different drift and dipole contributions.