First Attempt to Simulate the Shielded Button Measurements
with ECLOUD
 All material for this talk, including full sets of the analysis plots, may be obtained at www.lepp.cornell.edu/~critten/cesrta/ecloud/7apr10
Jim Crittenden
Cornell Laboratory for Accelerator-Based Sciences and Education
Electron Cloud Meeting
7 April 2010

---
Measurements of 16 March 2010
5.3 GeV, two bunches, 8 mA, 15E (TiN)
https://webdb.lepp.cornell.edu/elog/CTA+MS/528
Positrons
Electrons
The time scales are absolute, synchronized to the bunch passage.
The time resolution is subnanosecond, both rising and trailing edge.
The electron beam shows a remarkably sharper time structure.

---
Synchrotron Radiation Analysis of Pretzel-off CHESS optics
Positrons
Electrons
The direct synchrotron radiation photon rate is an order of magnitude smaller for electrons.

---
ECLOUD input parameters
  1.28e11 (8 mA)
  2
  n.a.
 4.2 (14 ns)
 e+: 18.8 e-: 18.8
 e+: 0.222 e-: 0.205
 e+: 0.0185 e-: 0.0191
 0.1
 e+: 1.00 e-: 0.118
   ( g / m / e )
n.a.
20%
 1.0 (0.9 t.s. & 0.1 rediff)
 400
SEY estimated for processed TiN.
Numerical parameters large: 1000 steps, 101 kicks, 250k m.p. per bunch.

---
Beampipe-averaged Cloud Density
Positrons
Electrons
The direct synchrotron radiation photon rate is an order of magnitude smaller for electrons
and the decay time between bunches is much greater.
But the beampipe-averaged density is only weakly related to the shielded button signal.

---
Comparison of Simulated Signal to Measurement
-- Positrons --
Measurement (Central Button)
ECLOUD Simulation
Simulation counts cloud charges in three adjacent 1-cm wide stripes centered on the top of the beampipe.
The angle of incidence is required to be less than 45 degrees (cosq > 0.7, probably not strict enough).
Any macroparticle contributing to the shielded button signal is removed from the cloud.

---
Comparison of Simulated Signal to Measurement
-- Electrons --
Measurement (Central Button)
ECLOUD Simulation
Many types of discrepancy for the case of the electron beam.
Particularly notable are the relative magnitudes of the two signals and the sharper time structure in the simulation.