Physics Scope and Work Plan for the Shielded-Pickup Measurements
-- Synchrotron Radiation Photon Distributions --
-- Photoelectron Production Parameters --
-- Secondary Yield Parameters --
--- 7 March: Added 3 slides for vacuum chamber comparisons under same beam conditions ---
Jim Crittenden
Cornell Laboratory for Accelerator-Based Sciences and Education
CesrTA Electron Cloud Simulation Coordination Meeting
3 March 2011

---
Example of a Witness Bunch Study: 9 May 2010
15W, Al v.c., 2.1 GeV, 3 mA/bunch e+ beam, 4-ns spacing increments
Superposition of 15 such traces
illustrating the sensitivity to cloud lifetime
Shielded pickup scope trace for two bunches
44 ns apart
The single bunch signal arises from photoelectrons produced on the bottom of the vacuum chamber.
Its shape is thus closely related to the photoelectron kinetic energy distribution modulo the beam kick.
The witness bunch signal includes the single-bunch signal as well as the that produced by cloud particles
accelerated into the shielded pickup by the kick from the witness bunch.

---
Sensitivity of the single bunch signal to the p.e. energy distribution
2.1 GeV, e+ beam, Ecritical = 0.23 keV
Power-law found to match 5.3 GeV
E P1 / ( 1 + E/E0 ) P2
Epeak, P1,P2 = 4 eV 3.6 5.2
Original ECLOUD
Gaussian with Epk, rms = 5 eV 5 eV
Lorentzian with Epeak, width = 5 eV, 7 eV
Not enough at high energy
Signal onset delayed
Much too high energy
Good match
Examples of photoelectron energy distributions modeled in ECLOUD.

---
Additional sensitivity of the witness bunch studies to
photoelectron azimuthal distributions
-- First experimental support for the SYNRAD3D model --
Uniform
SYNRAD3D
The SYNRAD3D azimuthal distribution is a remarkable improvement, both for the shape of the single-bunch signal and
for the shapes and relative sizes of the witness bunches at 4 and 32 ns.
This improvement arises primarily from the SYNRAD3D prediction of substantial p.e. production on the 'wrong side' of the vacuum chamber.

---
Spectrum analysis of the direct s.r. photons
using the solenoidal magnetic field
Example: 5.3 GeV 1 mA/bunch e+ beam, 40 Gauss
1
2
3
1
Time (ns)
2
Time (ns)
3
Time (ns)
The risetimes of the signals from the three buttons clearly show the differing acceptance at high photoelectron energy.
These measurements may also provide information on the production angular distribution.

---
 ECLOUD sensitivity to secondary electron yield parameters
3/27/10: 15E, TiN, 5.3 GeV, 5 mA/bunch e+ beam, 14-ns spacing
Correlation studies with ECLOUD have shown the secondary yield parameters to be decoupled. The first bunch signal arises primarily from photoelectrons.
The early witness bunch signal amplitudes depend primarily on the true and rediffused SEY components. The decrease in signal amplitude for late witness
bunches is closely related to the elastic yield parameter d0.
This example shows a preferred value for the TiN coating of d0=0.05. A similar value was found for amorphous carbon coatings, while the value for bare Al was 0.75.

---
Witness Bunch Study Data Sets
2010
Many systematic studies completed.
Photoelectron energy distributions determined for s.r. critical energies of 0.23, 0.34, 1.6, 2.4, 3.7, 5.6 keV.
Production analyses can begin.

---
Work Plan
ECLOUD analysis of the existing data sets (nonzero probability of a summer student)
Continue studies of systematics and parameter correlations
Witness bunch studies
Compile SEY parameter values for amorphous carbon, TiN and bare aluminum.
Test SYNRAD3D calculations of photon scattering (contingent on CESR v.c. modeling) .
Compile photoelectron energy distributions for scattered photons.
Solenoid field scans
Compile photoelectron energy distributions for direct photons. Since the photon energy distribution is well known it may be possible to derive energy-dependent quantum efficiencies.
Test sensitivity to the photoelectron production angular distribution.
Measurements for the upcoming data-taking periods in April and June
Repeat the above studies for the diamond-like carbon coated chamber at 15E
Measure horizontal beam-position dependence of the SPU signals

---
Electron cloud meeting 24 Nov 2010: Parameter correlation study
ECLOUD cloud lifetime sensitivity to elastic yield d0
Data set 3/27/2010: 5.3 GeV 5 mA/bunch e+ beam for 15W carbon-coated v.c.
Baseline parameters: 0.9 g /m/s, q.e. 5%, reflectivity 20%, dts = 0.7, Epk = 400 eV, dred = 0.1.
SPU signal scaled by factor 1.7. Elastic yield parameter d0 = 0.05 is the best match.

---
ECLOUD cloud lifetime sensitivity to elastic yield d0
Data set 5/17/2010: 5.3 GeV 3 mA/bunch e+ beam for 15W, Al v.c.
Baseline parameters: 0.9 g /m/s, q.e. 10%, reflectivity 20%, dts = 0.9, Epk = 400 eV, dred = 0.1.
SPU signal scaled by factor 1.1. Elastic yield parameter d0 = 0.75 is the best match.

---
Vacuum Chamber Comparison Under Same Beam Conditions
5.3 GeV Positron Beam
Witness bunch with 28-ns spacing
15W
15E
5 mA/bunch
The carbon coating
suppresses high-energy
photoelectrons compared
 to the TiN coating.
The results for the second
carbon-coated chamber
corroborate the
high-energy photoelectron
suppression relative
to TiN observed with the
first carbon chamber.
The q.e. for reflected
photons and the SEY
are both much smaller
for TiN compared to Al.
The 3-mA TiN witness
signal is a factor of 5
smaller than
for 5 mA/bunch.
(see slide 13)
3 mA/bunch
The second
carbon-coated chamber
shows conditioning effects
between 5/17 and 12/24,
primarily for the
quantum efficiency.

---
Vacuum Chamber Comparison Under Same Beam Conditions
5.3 GeV Electron Beam
Witness bunch with 28-ns spacing
15W
15E
5 mA/bunch
The carbon coating
suppresses photoelectron
production relative to
the TiN coating, but
the SEY may be higher.
Similar conclusions as
for the first carbon-coated
vacuum chamber.
The measurements with
the electron beam
confirm the much
smaller q.e. for reflected
photons and SEY
for TiN compared to Al
found with the positron
beam.
3 mA/bunch
The electron beam
measurements confirm
the processing effect for
the second carbon
vacuum chamber observed
with the positron beam.

---
Bunch Current Scan
5.3 GeV Positron Beam
Witness bunch with 14-ns spacing
The bunch current scan of 9/21
confirms the nonlinearity in the
TiN signal observed in the
vacuum chamber comparisons.
This strong nonlinearity of the witness bunch
signal relative to bunch current will provide
sensitivity to the energy dependence
of the secondary yield .
Remark from MAP: The AREAS of the
signals are linear with bunch current at
the 15% level, as would be expected
if primary photoelectrons dominated the
signal, in which case the SEY curve will
not affect it much. Simulations will tell.