DTC02 – DR 3.238km Lattice
Presenter
Cornell University
September 27, 2011 LCWS11
Global Design Effort

---
DTC02 Layout
Circumference = 3238.681m
Harmonic number =7022
710m straights
~ 6 phase trombone cells
60 – 2.1m long wigglers
wiggler period = 30cm
14-poles
Bmax = 2.16T
Space for 16 RF cavities
Cryostats for upper and lower
positron rings are interleaved

---
Arc Cell - FDBDF
Cell length = 10.93m
Bend length = 3.0m
75 cells/arc

---
DTC02 Lattice Functions
Arc
Arc
Inj-Ext
Straight
Wig-RF
Straight

---
RF Cells

---
Extraction Straight

---
Injection straight

---
Circumference Changing Chicane

---
Wiggler
30cm wiggler params
14 poles
30cm period
Wiggler length = 2.1m
Cell length = 7.56 m
30 wiggler cells
2 wiggler cells

---
 DTC02 Parameters

---
RF
The lattice can accommodate 16 RF cavities
If we assume 12 then:
     Voltage/ cavity in 10Hz mode is 1.64
     Power/coupler in 5Hz, high power mode is 300kW

---
Dynamic Aperture: 5 Hz
Periodic type wiggler model, includes vertical focusing and cubic nonlinearity

---
Dynamic Aperture:10 Hz
Periodic type wiggler model, includes vertical focusing and cubic nonlinearity

---
Magnet Count (Damping Ring)

---
Injection/Extraction
Positrons – injection from left, extraction to right
Electrons – injection from right, extraction to left
Midpoint between injection and extraction kickers is 2.56m from center of straight
Angle at entrance/exit of transfer lines with respect to storage ring straight = 240mrad

---
Injection/Extraction
Injection and extraction lines are identical
Angle with respect to damping ring straight = 240mrad