Baseline Damping Ring Lattice Design Status
Jim Crittenden
Cornell Laboratory for Accelerator-Based Sciences and Education
LCWS11
27 September 2011

---
DTC02 Layout
(D.L.Rubin)
Circumference = 3238.681 m
Harmonic number =7022
710-m straights
~ 6 phase trombone cells
Sixty 2.1-m long wigglers:
30-cm period, 14 poles
Bmax = 2.16T
Space for 16 RF cavities
The cryostats for upper and lower
positron rings are interleaved.

---
Arc Cell - FDBDF
Cell length = 10.93m
Bend length = 3.0m
75 cells/arc

---
DTC02 Lattice Functions
Arc
Arc
Inj-Ext
Straight
Wig-RF
Straight

---
RF Cells

---
Extraction Straight

---
Injection Straight

---
Circumference-Changing Chicane

---
Wiggler Cells
Wiggler parameters
14 poles
30-cm period
Wiggler length = 2.1m
Cell length = 7.56 m
30 wiggler cells
2 wiggler cells

---
DTC02 Parameters
	10 Hz(Low)	5 Hz (Low)	5 Hz (High)
Circumference [km]	3.23868	3.23868	3.23868
RF frequency [MHz]	650	650	650
tx/ty [ms]	13.5	24.1	24.1
tz [ms]	6.7	12.0	12.0
σz [mm]	6	6	6
σδ	0.134%	0.11%	0.11%
αp	3.3 X 10-4	3.3 X 10-4	3.3 X 10-4
γεx [μm]	4.6	5.4	5.4
RF [MV] (12 cavities) Total/cavity	19.7/1.64	14 /1.17	14/1.17
ξx/ξy	-50.9/-44.1	-51.3/-43.3	-51.3/-43.3
Wigglers: Ncells@B[T]	30@2.1	27@1.5	27@1.5
Energy loss/turn [MeV]	8.0	4.5	4.5
Sextupoles	3.34/-4.34	3.34/-4.23	3.34/-4.23
Power/RF coupler @400mA [kW]	267	150	300

---
RF Cavities
The lattice can accommodate 16 RF cavities
If we assume 12 cavities then:
     Voltage/cavity in 10 Hz mode is 1.64 MV
     Power/coupler in 5 Hz, high power mode is 300 kW

---
Dynamic Aperture 5 Hz
Periodic type wiggler model, includes vertical focusing and cubic nonlinearity

---
Dynamic Aperture 10 Hz
Periodic type wiggler model, includes vertical focusing and cubic nonlinearity

---
Magnet Count (Damping Ring)
	Length [m]	Strength	Number
Arc Dipoles	3	2.28 kG	150
Chicane dipoles	1	2.68 kG	28
Other dipoles	2	< 2.28 kG	4
Arc Quadrupoles	0.6	< 0.6 m-2	450
Quadrupoles in dispersion / suppressor and straights	0.3	< 0.55 m-2	211
Sextupoles	0.3	< 4.34 m-3	600
RF cavities	3	< 1.64 MV	12
Wigglers	2.1	2.16 T	60

---
Damping Wiggler Redesign
CESR-c Damping Ring Studies in the Context of the ILC Damping Ring Wigglers
PAC 2005
J.Urban and G.Dugan
Design Considerations and Modeling Results
for ILC Damping Ring Wigglers
Based on the CESR-c Superconducting Wiggler
PAC 2007
M.A.Palmer, J.A.Crittenden and J.Urban
Period reduced from 32 to 30 cm and number of poles increased from 12 to 14.
Gap reduced from 8.64 cm to 7.62 cm. Peak field increased from 2.0 to 2.16 T.

---
Wiggler Field Analytic Form for Symplectic Tracking
A Magnetic Field Model for Wigglers and Undulators, , PAC 2003, D. Sagan, J.A. Crittenden, D.L. Rubin and E. Forest
The field map has been posted on the ILC/CesrTA wiki.
A conceptual design for costing purposes is in preparation.
1200-term optimization underway.
Residuals presently at the level of a few gauss. The parameters have been posted on the wiki.

---
Vacuum System Design Effort
Work at Cornell directed towards:
  - Implementation of mitigation recommendations into the vacuum chambers
  - Need chamber profiles for next round of physics simulations
  - Need chamber and system conceptual design for costing

---
Wiggler Chamber Concept I
NEG strips
Clearing Electrode
E-beam weld locations
Copper Chamber

---
Wiggler Chamber Concept II
We are considering a scenario where 2 wigglers with a quad in center are assembled as a unit and then installed.
This would reduce the number of electrode chambers required.

---
Aluminum Dipole Chamber Concept
Radial inside of ring
Radial outside of ring
Locations of NEG strips

---
Vacuum System Summary
- Tasks underway
  - Concepts for drift, quadrupole, sextupole chambers in arcs
  - Pumping requirements for straights
    - Will in-situ bakeout of chambers in the
      straights be required?
    - What are our options?
  - Full ring wall profile for EC
    simulations
- Tasks to do
  - Photon stop & masks conceptual design in wiggler region
  - Full system concept for costing