Recent Electron Cloud Studies at CESRTA
Jim Crittenden
Cornell Laboratory for Accelerator-Based Sciences and Education
LCWS12
25 October 2012

---
EC Buildup R&D at CESRTA
- CESR Configuration
  - Damping ring layout
  - 4 dedicated EC experimental regions
  - Upgraded vacuum/EC instrumentation
  - Energy flexibility from 1.8 to 5.3 GeV
- EC Diagnostics and Mitigation
  - ~30 retarding field analyzers (RFAs) deployed
  - TE wave measurement capability in each experimental region
  - Time-resolving shielded pickups in two experimental locations
  - Four new time-resolving RFAs
  - Over 20 individual mitigation studies conducted in Phase I
    - 20 custom chambers
    - In situ SEY measurements
    - Follow-on studies in preparation for Phase II extension of program
Modeling for Extrapolation to ILC Damping Ring Design
Simulations of photon transport, including scattering (specular and diffuse) in detailed vacuum chamber models including antechambers
EC growth: establishing physics model parameters for EC growth modeling codes (POSINST, ECLOUD)

---
EC Buildup Detectors at CESRTA
L3 Electron cloud experimental region
PEP-II EC Hardware: Chicane, in situ SEY station
Four time-resolving RFA's
Field-free and quadrupole diagnostic chambers
New electron cloud experimental regions in arcs
(after 6 wigglers moved to L0 straight)
Locations for collaborator experimental vacuum chambers
equipped with RFAs and shielded pickup detectors
15W
15E
Custom vacuum chambers with RFAs and shielded pickup detectors
Uncoated aluminum, and TiN, amorphous carbon, diamond-like carbon coatings
30 RFA's in field-free regions, dipoles, quadrupoles, and wigglers

---
CESRTA RFA Design
Collectors
Beam pipe holes
Retarding grids
Beam pipe

---
RFA Measurements: Field-free Regions
Collector steady-state current density vs retarding voltage
(Cu chamber, Ibeam = 56 mA)

---
RFA Measurements: Dipole Field
Collector current density vs retarding voltage
(1.25 mA / bunch)
Collector current density vs bunch current
(1.25 -- 8 mA / bunch)
The RFA signal is sensitive to cloud photoelectrons and secondary electrons produced
 on the vacuum chamber wall near the vertical plane containing the beam.
At high bunch current the electrons are accelerated to energies greater than the secondary yield curve maximum,
resulting in the central depletion zone shown. The cloud splits into two vertical bands.

---
Secondary Electron Emission Model
The three secondary electron yield processes differ in their dependence on incident energy and produce electrons of differing kinetic energy distributions. The relative rates of these secondary emission processes depend on the vacuum chamber surface properties such as coating, roughness, grooves, as well as on beam conditioning.
Determination of these model parameters is critical for predicting performance limitations for future machines.

---
Drift Region RFA Data vs Simulation
J.R. Calvey et al, ECLOUD10, PAC11, IPAC11
  - RFA measurements provide data for validation of models for electron cloud build-up
  - Models require parameters describing surface phenomena: photon absorption site distributions (provided by synchrotron photon tracking code Synrad3D), photoelectron production, and secondary electron emission

---
Measurements of the Time Dependence
of Cloud Buildup Using Shielded Pickups
15W
15E
Custom vacuum chambers with RFAs and shielded pickup detectors
Uncoated aluminum, and TiN, amorphous carbon, and diamond-like carbon coatings

---
Shielded Pickup Design and Readout
10 kW
0.76 mm
diameter
Bias +50 V
8-bit
digitizing
oscilloscope
2 mm
X 100
0.1 µF
50 W
Detail
The pickup electrodes are shielded by the vacuum chamber hole pattern against the beam-induced signal.
The +50 V bias ensures that secondaries produced on the electrode do not escape.
The 8-bit digitized signal is an average over 8k triggers in time intervals of 0.1 ns.

---
Witness Bunch Method for Constraining Model Parameters
Example : 5/9/2010 2.1 GeV e+ 3 mA/bunch Al v.c. 15W
Shielded pickup scope trace
for two bunches 44 ns apart
Superposition of 15 such traces
illustrating the sensitivity to cloud lifetime
Leading bunch signal
from photoelectrons
produced on the bottom
of the vacuum chamber
Witness bunch signal
includes in addition cloud
electrons, mostly secondaries,
accelerated into the detector
by the beam.
The single bunch signal arises from photoelectrons produced on the bottom of the vacuum chamber.
Its shape is closely related to the photoelectron kinetic energy distribution and the beam kick.
The witness bunch signal includes the single-bunch signal as well as the that produced by cloud particles accelerated into the shielded pickup by the kick from the witness bunch. The witness signal is therefore sensitive to SEY.

---
Electron cloud buildup modeling code
ECLOUD
* Originated at CERN in the late 1990's
* Widespread application for PS, SPS, LHC, KEK, RHIC, ILC ...
* Under active development at Cornell since 2008
* Successful modeling of CESRTA tune shift measurements
* Interactive shielded pickup model implemented in 2010
* Full POSINST SEY functions added as option 2010-2012
* Flexible photoelectron energy distributions added 2011
* Synrad3D photon absorption distribution added 2011
Modeled Signal
Counting signal macroparticles in each time slice
gives the statistical uncertainty shown
Generation of photoelectrons
Production energy, angle
Azimuthal distribution (v.c. reflectivity)
Time-sliced cloud dynamics
Cloud space charge force
Beam kick
Magnetic fields
Secondary yield model
True secondaries (yields > 1!)
Rediffused secondaries (high energy)
Elastic reflection (dominates at low energy)
Shielded pickup model
Acceptance vs incident angle, energy
Signal charge removed from cloud
Non-signal charge creates secondaries

---
Modeled photoelectron
kinetic energy distribution
The shape of the signal from the leading bunch is determined by the photoelectron production energy distribution.
Two Power-Law Contributions
F(E) = E P1 / ( 1 + E/E0 ) P2
E0 = Epeak (P2-P1)/P1
This level of modeling accuracy was achieved with the photoelectron energy distribution shown below, using a sum of two power law distributions.
Epeak= 80 eV P1= 4 P2= 8.4
The high-energy component (22%) has a peak energy of 80 eV and an asymptotic power of 4.4. Its contribution to the signal is shown as yellow circles in the lower left plot.
Epeak= 4 eV P1= 4 P2= 6
The low-energy component (78%) has a peak energy of 4 eV and an asymptotic power of 2. It's contribution to the signal is shown as pink triangles.
Electron Cloud Buildup Models and Plans at CESRTA
JAC et al, LCWS11
Recent Developments in Modeling Time-resolved Shielded-pickup Measurements
of Electron Cloud Buildup at CESRTA
JAC et al, IPAC11

---
Constraints on the energy distribution of “true” secondary electrons
f(Esec) ~ Esec exp (-Esec/ESEY )
The time development of the cloud is directly dependent on secondary kinetic energies and therefore on the relative probabilities of the three secondary production processes:
1) True secondaries dominate at high incident energy and are produced at low energy
2) Rediffused secondaries are produced at energies ranging up to the incident energy
3) Elastic scattering dominates at low incident energy
The CESRTA Test Accelerator Electron Cloud Research Program Phase 1 Report
M.A.Palmer et al, August, 2012
Recent Developments in Modeling Time-resolved Shielded-pickup Measurements of Electron Cloud Buildup at CESRTA
JAC et al, IPAC11
Electron Cloud Buildup Models and Plans at CESRTA
JAC et al, LCWS11
The pulse shape for the 14-ns witness bunch signal sets a lower bound on the model parameter ESEY.

---
Beam conditioning effects on
an amorphous carbon coating
Recent Developments in Modeling Time-resolved Shielded-pickup Measurements
of Electron Cloud Buildup at CESRTA
JAC et al, IPAC11
Time-resolved Shielded-pickup Measurements and Modeling of
Beam Conditioning Effects on Electron Cloud Buildup at CESRTA
JAC et al, IPAC12
The beam conditioning effect for an amorphous carbon coating is primarily in quantum efficiency in both the
early and late conditioning processes.

---
Witness Bunch Study for Uncoated Aluminum 5/17/2010
15W 5.3 GeV 3 mA/bunch e+ 4-ns spacing
The later witness bunches provide sensitivity to the value for elastic yield.

---
Discriminating between the true and rediffused
secondary emission processeses
The rediffused secondary yield process determines the trailing edge of the signal from a single bunch.
This trailing edge is insensitive to d0 ,
as seen on the previous slide.
The late witness bunch signal used to determine d0 is also sensitive to the rediffused yield process.
The value for the rediffused yield of 20% for uncoated aluminum is consistent with the value determined using CESRTA coherent tune shift measurements (JAC et al, IPAC10)

---
ILC Damping Ring Lattice and Vacuum Chamber Design (JAC et al, IPAC12)
Recommendations for vacuum chamber mitigation techniques in wigglers, dipoles, quadrupoles, sextupoles and field free regions were determined at the ECLOUD'10 workshop.
The antechamber design was modified according to Synrad3D photon transport calculations.
Calculated photon absorption site distributions were used as input to cloud buildup models.

---
ILC Damping Ring
Electron Cloud Buildup Modeling
Field-free Regions
Solenoids off
Field-free Regions
Solenoids on
Quadrupoles
Sextupoles
Cloud densities calculated in beam region were used as input to head-tail instability modeling code to provide results for the ILC TDR.

---
New Time-Resolved RFA's in L3
Vacuum chambers bare and TiN-coated, smooth and grooved

---
New Time-Resolved RFA's in PEP-II Chicane Dipole Field On/Off
Chicane dipole field off
Central collectors dominate.
Chicane dipole field 45 G
Central collectors show a depletion zone.
This is known to arise from the peak of the
SEY curve and provides information on Emax.

---
Summary and Near-Term Plans
Summary
The time-averaged RFA measurements and the time-resolved measurements shielded pickup of cloud buildup provide remarkable discriminating power between photoelectron and secondary electron production processes. They also provide information distinguishing the various processes contributing to secondary electron production.
The time-resolved information is very sensitive to the production kinematics for both photoelectrons and secondary electrons.
Cloud buildup models including photoelectron production, secondary emission and cloud dynamics have been developed and validated by comparing them to a wide variety of RFA and shielded pickup measurements. These necessitated the development of synchrotron radiation photon tracking modeling to provide the distribution of photon absorption sites for an arbitrary lattice design. These modeling techniques have been used to make quantitative estimates of electron cloud buildup in the ILC positron damping ring.
Near-term Plans
Innovative new detectors combining the time-resolving capability of the shielded pickups with the segmentation and energy sensitivity of the RFAs have been designed, built and installed in four custom aluminum vacuum chambers, bare andTiN-coated, smooth and grooved. Initial data-taking and modeling has begun.