Bug Found and Fixed in BMAD Calculations of Orbit Distortions Induced by Cavity Offsets
--
Example of HOM Kicks Distorting Orbit
in the CERL 8.2 Lattice and Effectiveness of Orbit Correction
J.A. Crittenden, Georg Hoffstaetter, Chris Mayes and David Sagan
Cornell Laboratory for Accelerator-Based Sciences and Education
ERL@CESR Meeting
18 November 2010

---
Effect of bug on full CERL8.2 equilibrium orbit calculation
with 5 HOMS in all cavities and 0.3 mm rms offsets
Calculated orbit distortion before fix
(see talk of 23 September 2010)
After fix
This bug affected ONLY cases of HOM elements in RF cavities with position offsets.

---
CERL 8.2 calculation with 0.3 mm randomized cavity offsets
5 HOMs (MUL 2009) in each of 384 cavities
The frequency spread is 0.4%, i.e. 10-12 Mhz.
The randomization of the HOM frequencies is limited to +- 3sf.

---
Orbit correction in CERL 8.2
with 5 HOMS in all cavities and 0.3 mm rms offsets
Before orbit correction
After orbit correction
Correction only possible downstream of kickers.
NB: Orbit distortion is much smaller than the cavity offsets.

---
Equilibrium HOM kicks with and without orbit correction
The effect of the orbit correction is negligible, because the cavity offsets are much larger.
Let's apply unrealistically large HOM kicks to see their effect and the effect of the orbit correction.

---
Resonant HOM: 2.6 GHz with R/Q raised factor 200 to 4e6 ohm/m2
with and without orbit correction
The orbit correction works well, despite the randomized HOM frequencies.
NB: The offsets are random, but the same in each cavity for the ten cases plotted here.

---
Resonant HOM: 2.6 GHz with R/Q raised factor 200 to 4e6 ohm/m2
with and without orbit correction
The HOM kicks are now as high as 600 kV.
The orbit correction now works well, since the orbit distortions are larger than the offsets.

---
Analysis now includes calculation of HOM power
dU/dt = VT2 wl 2 / ( Q (R/Q) c2 )
HOM kicks of 600 kV correspond to power values of 16 kW in this exaggerated example.
The orbit correction reduces the power by an order of magnitude.
The nominal value for (R/Q) of 2e4 W /m2 reduces the stored HOM power to 8 W,
which is within the specification of 20 W, even in this resonant case wl = 2w0 .