## Slide 1: CesrTA Future Plans
David Rubin
September 11, 2012

## Slide 2: Summary- Electron Cloud R&D
CESR converted for low emittance operation
Developed and implemented a dozen lattice configurations for multiple energies, emittances, with varying numbers of wigglers, etc.
Instrumented storage ring to study electron cloud growth and mitigation
Anchored electron cloud models with extensive and complementary measurements
Recommended complete set of mitigations for ILC damping ring
Used models to evaluate tolerance of ILC positron ring to electron cloud

## Slide 3: Summary – Low emittance
Instrumented CESR for simultaneous measurement of bunch height, width and length
Developed techniques for routine lattice correction and emittance tuning
Exploited instrumentation and flexibility to make most extensive measurements to date of Intra-beam scattering in an electron/positron ring

## Slide 4: Outstanding questions and investigations
Completeness of electron cloud model
Cloud induced emittance growth and instabilities
Long lived cloud in quadrupoles/wigglers (precursor studies)
TE wave measurement technique
Minimum vertical emittance
  Sources of emittance dilution
  Emittance tuning techniques
X-ray beam size measurement
  optimization/interpretation of coded aperture images
Visible light beam size measurement
  horizontal and vertical – turn by turn
Optical and Xray diffraction radiation beam size monitor
Intra-beam scattering
Fast Ion instability

## Slide 5: Electron cloud model
Is there a self consistent set of model parameters ?
  Fit of model to measured tune shifts in a long train constrains model parameters
  Simultaneous fits to multiple data sets with varying beam current, bunch configuration, beam energy, beam species further constrains parameters and tests the completeness of the model
  Similarly, RFA and SPU measurements can be fit to ecloud models with different sensitivities to the various parameters
  Time resolving RFA’s (very recently installed) will give complementary data that can likewise be fit to the model
  Our goal is simultaneous fit of all data sets
  (RFA,SPU, tune shifts) to best constrain parameters and establish that the model does (or does not) include all of the relevant physics consistent with SEY data

## Slide 6: Electron cloud model
Photon Reflectivity
Development of cloud depends on nature of scattering of synchrotron radiation photons
Angular distribution of scattering depends on details of the surface of scatter on the scale of photon wavelength
That dependence is parameterized in the model
Reflectivity collaboration aims to measure dependence on
- Surface material and roughness
- Photon energy
- Angle of incidence

## Slide 7: Electron cloud - dynamics
Instabilities and emittance blow up
  We observe cloud induced head tail instability and emittance dilution
  Connection between the two is not entirely clear. Does head-tail instability contribute to emittance growth or are the phenomena unrelated ?
  Simulations (CMAD, PHETS) and analytic calculations are in rough agreement with measurement of both growth and instability – although not in detail
  We aim to better understand the cause of sub-threshold emittance growth, connection to instability, nature of instability
  We would like to measure internal bunch motion

## Slide 8: Electron cloud - dynamics
Instrumentation for investigation of instability
xBSM bunch slicing
  Measure vertical position and size versus longitudinal position along bunch
  Fast diode array – 35 ps rise time
  4 size/position samples along the ~ 10 mm (30 ps) long bunch at 10 ps intervals
  Component testing beginning this fall

## Slide 9: Bunch slicing with xBSM
High speed
Diode array
Multi channel data acquisition system with individual phase delay

## Slide 10: Electron cloud dynamics
Simulation of bunch/cloud interaction
  Simulations (PHETS, CMAD) computationally intensive
  Calculations of thresholds for instabilities and emittance growth
    Typically based on hundreds of turns (fraction of a damping time)
    Limited to cloud within 20 σ of beam
  We need more efficient algorithms, and implementations to get at all of the physics

## Slide 11: Long lived electron cloud
Observation of Blowup of lead bunch
  Effect is mitigated with the help of a precursor bunch
  Depends on bunch spacing, number of bunches, total current, . . .
  Hypothesis
  Long lived cloud that accumulates along beam line in quadrupoles and/or wigglers, and is blown away by the precursor bunch
  Evidence
  The relatively high current measured in the quadrupole RFA suggests buildup over multiple turns
  3-D modeling of cloud in wigglers indicates that electrons are trapped in strong longitudinal field component

## Slide 12: Long lived electron cloud
We plan to test that hypothesis with
  Simulation:
    Simulation of multi-turn effects is computationally intensive
    3 D model may be required if longitudinal magnetic fields in wigglers, or in fringing fields of quadrupoles are important
  Instrumentation: Time Resolving RFA in quadrupole
  Measurements:
    Investigate dependence on various machine parameters, bunch configurations, species, etc.
    How do other features (tune shifts, internal bunch motion) respond to precursor
A long lived cloud that is trapped in quadrupoles could
have a significant impact on positron rings.

## Slide 13: TE wave measurement technique
Noninvasive
  No special in vacuum hardware
  (Couple to TE wave via BPM buttons)
  Possibility of measurement of transverse distribution of cloud density
  Requires:
  Better understand relation of side band amplitude to cloud density
  Details of spectrum of trapped modes

## Slide 14: Emittance
We have achieved 10-15 pm-rad
Theoretical zero current limit (quantum limit) is nearly 100 times smaller
Measured residual vertical dispersion and coupling can not account for observed vertical emittance.
Evidently there are other sources of emittance dilution
  Magnet motion, detector motion, unstable corrector magnet currents, noise coupled to the beam through RF system, . . .
  We observe significant motion at high frequencies. (Betatron tunes are self excited)
  Perhaps there is an electron cloud or ion effect that is relevant even at very low bunch current
  Our goal is to continue to identify and mitigate sources of emittance dilution and to approach the quantum limit

## Slide 15: Emittance dilution due to beam motion
Turn by turn xBSM data
~30 micron variation in centroid position
~ 3 micron variation in beam size
FFT identifies vertical betatron motion
We need to identify (and eliminate) source of excitation

## Slide 16: Emittance dilution due to beam motion
IBS run
High current
Low current

## Slide 17: Emittance
Real time emittance tuning
  Measurement of lattice errors via resonant excitation affords the possibility to continuously monitor betatron phase/coupling and vertical dispersion (as well as orbit)
  Drive a witness bunch using gated tune tracker at 3 normal mode frequencies
  Turn by turn position at each BPM
=> Orbit, phase, coupling, dispersion

## Slide 18: X-ray beam size monitor
Optimize coded aperture for
  X-ray energy spectrum
  Bunch size
  Intensity
Match x-ray energy to diode and optimize layout of diode array
Refine fitting techniques for extracting size from coded aperture data
All vacuum x-ray beam lines for full sensitivity across the spectrum

## Slide 19: Visible light beam size monitor
Developing turn by turn capability based on linear array of photomultiplier tubes
Exploring measurement of vertical beam size
  Interferometry
  Polarization
  As complement and check of xray beam size monitor

## Slide 20: ODR/XDR
Goal
  Measure vertical beam size with 1μm resolution
  Phase I – optical diffraction radiation (Dec. 2012)
  - 400μm and 1 mm diffraction slit width
  => image odr pattern from ~ 20 μm beam
  Phase II – x-ray diffraction radiation (Dec. 2013)
  - 10 μm slit width
  => image xdr pattern from ~ 1 μm beam
  Depends on installation of mini-β insert
  to achieve 1 μm beam in CESR

## Slide 21: Collective effects
As we continue to achieve smaller vertical emittance, our sensitivity to collective effects (especially emittance diluting effects) is enhanced.

## Slide 22: Intra-beam scattering
  Continue to explore IBS and test theory with ever smaller zero current emittance
  IBS has strong energy dependence.
    Measurements at 1.8 and 2.3GeV planned for December 2012, will bracket the 2.1GeV data
    Preliminary tests at 1.8/2.3 to explore dependence of xBSM on xray spectrum have been completed
  Anomalous blowup of vertical beam size at high current ?
  Dependence on dispersion in RF ?
  New capability in next run =>
  Synchronized single pass measurement of horizontal
  and vertical beam size

## Slide 23: Fast Ion
Fast-ion instability
  CesrTA well instrumented for study of fast-ion effect
  Sensitivity expected to increase as vertical emittance shrinks
  xBSM and beam position monitors provides bunch by bunch and turn by turn measure of vertical emittance and position spectra (similarly to investigation of ecloud emittance growth)
  We plan direct measure of fast ion instability, and the threshold for emittance growth.

## Slide 24: CesrTA Students
Graduate students
  J. Calvey, N. Eggert, M. Ehrlichman, R. Helms, W. Hopkins, B. Kreis, J. Shanks, J. Urban, Y. Yariv
Undergraduates
  K. Butler, H. Kaminsky, J. Kim, Z. Leong, H. Liu, J. Livezey, J. Makita, M. McDonald, G. Ramirez, S. Santos, R. Schwartz, S. Vishniakou, W. Whitney, H. Williams, L. Fabrizzio, M. Randazzo, R.Campbell, S. Roy, J. Ginsberg
REU (Research Experience for Undergraduates)
  D. Carmody, C. Cude, P. Kehayias, M. Lawson, B. Carlson, D. Gonnella, E. Wilkinson, L. Hales, K. Hammond, N. Omcikus, Z. Warecki, J. Bonilla, D. Duggins, E. Hemingway, K. Williams

## Slide 25: Funding
Phase I (2008−2011)
  80% NSF(CESR Conversion), 20% DOE (ILC-ART)
  Total of 240 days dedicated CESR running time
Phase II (2011 – 2014)
  NSF (Lepton Collider)
  40 days dedicated CESR running time/year
Phase III (2014 − ?) Proposal due 9/13
  Request
    Beam physics and instrumentation for low emittance electron/positron rings
    40 days/year machine time
    Details depend on CHESS upgrade plans

## Slide 26: Conclusion
CesrTA is a well instrumented laboratory for investigation of beam physics of low emittance rings
  Flexible optics – mature interface of design/optimization/measurement/analysis tools (BMAD/CESRV/Tao)
  State of the art instrumentation, and ongoing development
  Sophisticated modeling and simulation capability based on integrated library of accelerator modeling code (BMAD)
Contributions
  Electron cloud physics, emittance tuning, intra-beam scattering, materials characterization, beam instrumentation
Collaborative effort (14 institutions)
Accelerator physics education
Compelling program of beam physics, experiment and theory

## Slide 27: End
Thank you for your attention