## Slide 1: Introduction to CesrTA
David Rubin
September 11, 2012

## Slide 2: Questions
Consider the positron storage ring:
  What is the threshold beam current for emittance dilution and instability due to the electron cloud ?
  What are the most effective techniques for mitigating the growth of the electron cloud ?
  What are the relevant material properties of the mitigations?
  How do we extrapolate our findings to other machines ?

## Slide 3: Program: Question 1
To address the first question (emittance dilution threshold ?)
  Create low emittance (both horizontal and vertical) CESR configuration so that we can explore the beam physics in the appropriate regime =>
    Superconducting damping wigglers to reduce emittance
    Instrumentation for beam based measurement and optics correction, to minimize residual coupling and dispersion
    Instrumentation for measuring emittance
  Develop techniques for generating an electron cloud of arbitrary (ring averaged) density
  Instrumentation to measure emittance growth and instabilities as a function of the cloud density

## Slide 4: Program Questions 2-3
To address the second (effectiveness of mitigations ?)
  Detectors for measuring local electron cloud density in a controlled environment including:
    Flux of synchrotron radiation
    External magnetic field (dipole, quadrupole, wiggler, drift)
    Vacuum chamber geometry and surface treatment
    Beam energy, current and bunch configuration
  (Retarding field analyzers, shielded pickups, TE wave)
And the third (material properties ?)
  Detectors that can provide temporal information about the growth and decay of the cloud
  ( Shielded pickups and time resolving RFAs)

## Slide 5: Question 4 – Extrapolation
Synchrotron radiation photons strike chamber walls emitting photo-electrons.
Electrons are accelerated by the circulating positron bunches into the opposite wall, producing secondaries
Interaction of the positron beam with the accumulating cloud generates instabilities and dilutes vertical emittance
Electron Cloud

## Slide 6: 4 – Extrapolation to Other Machines
Physics of the electron cloud is incorporated into models
  The “Complete” model includes
Emission of photons from circulating positrons
Tracking of photons to the vacuum chamber. Generation of a photoelectron, or a reflection. If reflected continue tracking.
Simulation of the emission of photoelectrons at the photon-wall absorption point.
Evaluation of forces that act on the electrons (from the beam, space-charge and external fields).
Application of forces to the electrons and propagation of electron trajectories.
Simulation of secondary emission as the electrons hit the walls of the chamber.
Many details are parameterized in the model:
  Dependence of photon scattering angle on chamber surface (roughness). (Experimental program to verify reflectivity model is underway – Reflectivity collaboration)
  Quantum efficiency, angular and energy distribution of photo-electrons depends on photon energy and chamber surface properties
  Secondary emission depends on primary energy and incident angle as well as surface chemistry
Measurements inform the models and constrain the parameters
The models are the basis of the simulations that predict storage ring performance

## Slide 7
CESR Conversion

## Slide 8: CESR Conversion
Reconfigure CESR layout for low emittance operation
Develop/install instrumentation for measuring electron cloud
  Retarding field analyzers, - measurement of local density, spatial and energy distribution of the cloud
  Shielded pickups – local measurement of time evolution of the cloud
  TE-wave – semi-local measurement of density
  Bunch dependent tune shifts (global measure of cloud density)
Develop/install instrumentation for tuning low emittance (correcting β-phase, coupling, dispersion) and measuring effect of cloud on the beam
  High bandwidth/high precision beam position monitors
  Turn by turn/bunch by bunch x-ray beam size monitor (to measure vertical emittance)
Deploy survey reference grid for routine magnet alignment
Develop/install instrument for direct measurement of SEY of materials in storage ring environment

## Slide 9: CESR Conversion - constraint
Preserve compatibility with CHESS x-ray operation.
Transition from CesrTA low emittance single beam optics, to CHESS electron/positron configuration must be routine (1-2 hours)
Gate valves suitably deployed to minimize effect on CESR vacuum and CHESS operation when swapping test chambers

## Slide 10: Low Emittance
Machine Layout, Optics and Instrumentation for Low Emittance operation

## Slide 11: CESR Conversion – Low Emittance Optics
CESR lattice has long dipoles and a relatively low density of quadrupoles
=> relatively high emittance
To attain low emittance we rely on damping wigglers
At 2GeV, the 12, 1.3m long, 1.9T superconducting wigglers, decrease radiation damping time by 10 from 0.5 secs to 50 msec.
=> 4 fold reduction in horizontal emittance providing we can eliminate dispersion
To that end we re-locate 6 wigglers from arc to L0 straight.
And design optics with the appropriate constraints

## Slide 12: Low emittance lattice functions
E = 2.1 GeV
εx =3 nm-rad
Flexible magnetic optics
All 100 quadrupoles and 78 sextupoles are independently powered
More than a dozen distinct lattice configurations for operation at energies from 1.8 - 5.3 GeV have been implemented and used for various studies

## Slide 13: CESR Conversion
Wigglers moved from 15E/W to L0. Mitigations tested in L0 wigglers
Available space at 15E/W used to test mitigations in field free region
with SPU, RFA, TE-wave – dipole RFA
L3 Instrumentation
RFAs, dipole chicane, Time Resolving RFA, in-situ SEY, vBSM, TE-wave
Installed 2009-2012
Wigglers relocated to
L0, summer 2008

## Slide 14: Damping wigglers
Damping wigglers redeployed to zero dispersion straight
Wigglers instrumented with mitigations and RFAs

## Slide 15: Precision beam position monitors
Turn by turn/bunch by bunch
~10 micron single pass precision
Routine tuning
for low emittance is essential to the experimental program.
Beam based characterization of machine optics depends on high bandwidth/high precision beam position monitors.
Upgrade to digital readout electronics completed 2010

## Slide 16: Xray beam size monitor
Xray beam size monitor
- Measure vertical beam size to ~ 10 microns => vertical emittance
- Turn by turn/bunch by bunch to 4 ns => bunch dependent emittance
xBSM Commissioning – Positrons 2009-2010, Electrons 2011

## Slide 17: Visible light beam size monitor
Visible light beam size monitor
- Double slit interferometer => horizontal beam size (emittance and energy spread)
- Streak camera => bunch length
Streak camera - 2009
Horizontal beam size monitor - 2011
e-
e+

## Slide 18: Visible light beam size monitor
Schematic of visible light optics
Optical path length 17m from source at B48 to camera

## Slide 19: Low emittance configuration
Wigglers relocated to zero dispersion straight. (L0)
Survey reference system established, and magnet alignment completed
Instrumention deployed for tuning low emittance with capability to measure
  Turn by turn position
  Width, height, length of single bunch
  And turn by turn and bunch by bunch measure of vertical size

## Slide 20: Electron cloud instrumentation
Instrumentation for measuring electron cloud and characterizing mitigations

## Slide 21: Retarding field analyzers
Measures the energy spectrum of the time-average cloud current which impacts the chamber wall.
Most devices are segmented, so that some position information is also available.
Placed in drifts, dipoles, quadrupoles, and wigglers.
In chambers with mitigations, RFAs measure their effectiveness
Local measurement of time averaged flux of
electrons into wall of chamber

## Slide 22: Retarding field analyzers
Four wigglers are instrumented with RFAs
  Bare Cu
  TiN coated
  Grooves
  Clearing electrode
Each wiggler has three RFAs
Groove tips/valley radius < 0.002” !!

## Slide 23: Wiggler mitigations
Clearing electrode
Grooved copper insert

## Slide 24: Shielded pickup
Shielded pickups have nanosecond temporal resolution and inform time development and decay of cloud

## Slide 25: Experimental region 15W
Chambers with various mitigations are tested in 15W and 15E regions
=> providing comparison in standardized synchrotron radiation environment

## Slide 26: Electron Cloud Instrumentation
Wigglers moved from 15E/W to L0. Mitigations tested in L0 wigglers
Available space at 15E/W used to test mitigations in field free region
with SPU, RFA, TE-wave – dipole RFA
L3 Instrumentation
RFAs, dipole chicane, Time Resolving RFA, in-situ SEY, vBSM, TE-wave
Installed 2009-2012
Wigglers relocated to
L0, summer 2008

## Slide 27: Tested Mitigations
2009-2012

## Slide 28: Ecloud model – SEY measurement
Direct measurement of secondary
emission yield, including angular and energy dependence and
the effect of beam processing
Positron beam
Electron gun

## Slide 29: L3 instrumentation

## Slide 30: ILC positron damping ring
Contributions to ILC DR design - 2012
  Specification of vacuum chamber and mitigations for the ILC damping ring, based on CesrTA measurements
  Electron cloud simulation codes
    Developed in parallel to CesrTA experimental program,
    Benchmarked against CesrTA data
  That demonstrate that with the recommended
  mitigations, the electron cloud density will be well
  below threshold for emittance blowup
  Emittance tuning methodology developed for CesrTA is used to establish damping ring alignment and instrumentation specifications

## Slide 31: Beyond electron cloud
Intra-beam scattering
  Tuning techniques routinely yield ~ 10-15 pm-rad vertical emittance
  Instrumentation for measuring multi-bunch size and spectra is well suited to investigate collective effects (not just electron cloud)
  In low emittance CesrTA, 2GeV optics, intra-beam scattering makes significant (measurable) contribution to equilibrium beam size
  Measurements with both particle species allow us to distinguish electron cloud, ion, “other” effects
  And we have investigated IBS in some detail (2011-2012)

## Slide 32: Machine Studies TIme
  Nearly 240 days of dedicated studies time (2008 – 2012)
  Approximately one dozen lattice configurations implemented, tuned, tested
  With many dozens of “knobs” to adjust coupling, dispersion, horizontal & vertical emittance, beta …
  Experiments at 1.8, 2.1, 2.3, 3.0, 4.0, 5.3 GeV
  with both electrons and positrons
  Extensive measurements of ecloud, and low emittance beam physics

## Slide 33: Today’s Agenda
Instrumentation – John Sikora
SEY and RFA studies – Walter Hartung
Shielded Pickup studies – Jim Crittenden
Electron cloud beam dynamics studies – Gerry Dugan
Emittance tuning – Jim Shanks
Intra-beam scattering – Mike Ehrlichman
CesrTA Collaboration – Mike Billing
Super KEK-B ecloud mitigation and instrumentation - John Flanagan
Future plans – D. Rubin

## Slide 34: End
Thank you for your attention

## Slide 35: Low Emittance Optics
Exploit damping wigglers to reduce emitttance
At 2.0 GeV, 12-1.3m long 1.9T superconducting wigglers increase radiation damping rate 2/sec to 20/second.
If the wigglers are in a zero dispersion straight, there is an (almost) corresponding decrease in horizontal emittance.
Not quite because the wigglers themselves generate dispersion internally.
=>2.5 - 3 nm-rad

## Slide 36: CesrTA Program Goals
Electron cloud
  Mitigation
    Material properties: SEY, QE, beam processing, durability
  Modeling
    Cloud growth and beam-cloud interactions
  Dynamics
    Cloud induced tune shift, emittance dilution, instability
  To answer the question: For a given vacuum chamber design, what is the threshold current for emittance dilution and instability from the electron cloud?
Emittance tuning
  To determine sensitivity of low emittance beams to electron cloud effects, in a variety of lattice configurations (beam energy, horizontal emittance etc) we need set of beam based measurements and correction techniques for routine application
  Requires precision bpm to measure residual coupling and vertical dispersion, and beam size monitors for measuring emittance and a good understanding of systematic measurement errors
Collective effects
  While the electron cloud has been the principle focus of the effort, CesrTA is now well instrumented for exploring other collective effects including intr-beam scattering, fast ion instability, and limits to ultra-low emittance operation

## Slide 39: Introduction
Goals of the CesrTA R&D program
Emittance tuning
Electron cloud research
Intra-beam scattering
ILC positron damping ring
CESR conversion
Summary and plan for the day