## Slide 1
Kicker Status
Collaboration Meeting
November 19, 2015
David Rubin for
Alexander Mikhailichenko & SeungCheon Kim & Andre Frankenthal

## Slide 2: Kicker Status
Blumlein pulse forming network
Kicker plates and trolley rails
Power Supply
Controls
Pulse characteristics

## Slide 3: Storage Ring Kicker Requirements
Kickers steer injected muons onto the closed orbit of the storage ring
Requirements:
Kick angle ~ 10.8 to 12.8 mrad
Kicker B-field ~ 285 to 336 Gauss
Integrated B-field ~ 1.11 to 1.31 kG-m
Pulse width(τwid)
120ns < τwid < 149ns
Repetition rate
~100Hz peak, 12Hz average
3 – 1.3m kickers
d = 77 mm, R=7112 mm
kick angle q = d/R = 10.8 mrad
trev = 149 ns

## Slide 4
insulator
thyratron
Blumlein Pulse Forming Network
D = 9m
= 4.7 (Castor oil)
=> t = 120ns
blumlein
Direction of kick
9m

## Slide 5
Blumlein
3- 9m long triaxial tubes
thyratron
Coupling to 4 50W coax
Central conductor

## Slide 6
68 flanges manufactured by Hancock Precision Inc. received
Plan to place order for tubes in December
With radii fine tuned to improve impedance match
Blumlein implementation

## Slide 7
New cage for kicker plates (127 cm long)
Kicker Cage – Plates - Rails

## Slide 8: Kicker plates – rails - trolley

## Slide 9
Kicker cage, plate, rail assembly will be tested in g-2 vacuum chamber in December
System Test

## Slide 10
Electronics - Charging Circuit
SCR — Silicon Controlled Rectifier -Thyristor
40 kHz switching device
The time between “charge now” and the thyratron triggering ~ 2 ms
“Inhibit” input
thyratron
5kW

## Slide 11: Electronics
For each of three kickers
Thyratron driver
(heater, reservoir, trigger)
Charging supply
High voltage supply
High voltage transformer
Thyratron
On hand at Cornell
1 thyratron driver (commercially available)
3 charging supplies
3 high voltage supplies
3 transformers (some modification required)
2 thyratrons

## Slide 12
Transformer tanks

## Slide 13: Kicker Control and Monitoring
Control
Thyratron driver - on/off
High voltage supply - on/off
Oil pump- on/off
Flourinert pump – on/off
Tunable parameters
Thyratron heater
Thyratron gas reservoir
Charging voltage => kicker field
Triggers
High voltage inhibit (HV to capacitors)
Charging thyristor (Cap bank to HV transformer)
Thyratron trigger
Monitoring
Thyratron heater current and voltage
and reservoir current and voltage
Blumlein charging voltage and
current(~100ms time scale) digitized
Oil flow gauge
Kicker Current
and Kicker B-field (Cornell digitizer)
Interlocks
Oil flow
Thyratron heater timer
etc.
X 3

## Slide 14
Control and Monitoring
Web interface to Intel Galileo microprocessor via ethernet

## Slide 15
Operating and programming panel
Arduino 2560
Prototype Microprocessor Control

## Slide 16
Test Triggers
Trigger pulses programmed in microprocessor

## Slide 17
Pulse from current monitor (upper graph); optical monitor (lower graph).
(Cornell digitizer)
Kicker Pulse
100 ns/div

## Slide 18
Moment of thyratron triggering
Current in primary windings
(Power Designs CVT-1A)
Voltage applied to Blumlein
(Voltage at secondary windings)
Current in secondary windings
Charging transformer characteristics contributing to signal after main pulse?
Charging current and voltage
(Galileo digitizer)

## Slide 19
Pearson 3212; 50 kV; 4kA; 12 Hz, Full length Kicker ≈127 cm (50”)
The tail is generated by impedance mismatch?

## Slide 20: Kicker pulse
Representation of kicker pulse for simulation

## Slide 21: Kicker pulse
Test kicker effectiveness with simulation – compare 4 configurations
4-Uniform field/120ns rectangular pulse (ideal)
3-Curved plates/120ns rectangular pulse
2-Curved plates/measured pulse less tail
1- Curved plates/ measured pulse with tail (actual)
Capture efficiency reduced 17% due to imperfections of kick
Temporal non-uniformity of kicker pulse can introduce early to late systematic

## Slide 22
Proposed Impedance matching tuner
Includes resistor ( ~ 500 Ω) and capacitance or diode
Impedance Matching Tuner

## Slide 23
Faraday magnetometer

## Slide 24: END

## Slide 25
New pulser plate made for replacement of pulsed PS lost at Fermilab

## Slide 27
Blumlein Pulse Forming Network
Blumlein
voltage at load is equal to charging voltage
Base of switch (thyratron) at ground
Simple transmission line
voltage at load is ½ charging voltage
Base of switch floats
Pulse length

## Slide 28: Blumlein schematic
12.5 Ohm Blumlein
5000A X 12.5W = 62.5kV
Four parallel 50 W coaxial cables couple 12.5W
Blumlein to load

## Slide 29: Thyratron
Blumlein properties
Vmagnet = Vthyratron
Imagnet = ½ Ithyratron
Thyratron | CX1725X
Peak Voltage [kV] | 70
Peak Current [kA] | 15
dI/dt [kA/ms] | >300
Repetition rate [Hz] | 2000
Grids | 2
10.8mrad kick corresponds to
=> 5000 A (E989 kicker plates)
=> 62.5 kV with 12.5 W load
CX1725X – 62.5 kV and 10kA at thyratron required to deliver 5kA to 12.5W load
at 100 Hz with rise time < 20 ns ✓

## Slide 30
12.5 Ω Blumlein triaxial transmission line
Vacuum chamber with kicker magnet
50 W coax

## Slide 31: Thyratron switch

## Slide 32: Coupling to magnet
4 load resistors
(12.5Ω equivalent)
4 50Ω coaxial cables
Vacuum chamber
flourinert

## Slide 33
Kicker chamber
Magnetometer laser
Vacuum pump
Load resistors in flourinert
4 parallel 50Ω cables

## Slide 34
Pulse characteristics
Broader flat top can be obtained with
Longer Blumlein
Shorter kickers (and additional kickers to achieve integrated kick)
Fine tuning of thyratron gas pressure
Compensation of mismatched lengths of Blumlein transmission lines
Tail can be reduced with
Better matching of blumlein, cables, and load
Kilovac switch to eliminate bleed through of charging transformer
Temporal non-uniformity of kicker pulse can introduce early to late systematic
(SeungCheon Kim – Wednesday talk)

## Slide 35
Blumlein Pulse Forming Network
Blumlein
voltage at load is equal to charging voltage
Base of switch (thyratron) at ground
Simple transmission line
voltage at load is ½ charging voltage
Base of switch floats
Pulse length

## Slide 37: Thyratron and charging input