## Slide 1: Modeling Quad Scraping
D. Rubin
S. Kim
September 22, 2016

## Slide 2
E821 quad scraping strategy:
At injection, inner and outer and top and bottom quad plates are powered asymmetrically
The closed orbit is displaced from the center of the storage volume by about 2.5mm.
The effective aperture is reduced by the offset of the closed orbit – so that muons outside the reduced aperture are scraped off and removed from the distribution
Quad symmetry is restored after 30 ms (200 turns).
Closed orbit is restored to the midplane and magic radius.
Leaving 1.25 mm clearance between the extreme of the distribution and the aperture as defined by the collimators

## Slide 4
Modeling quadrupoles with independently powered plates
Solve Laplace eqn for quad with a single plate at voltage and the remaining 3 at ground – for each of the four plates in turn
=> 4 maps
Linear combination of the 4 maps scaled by relative voltage yields effective dipole kick and quadrupole focusing

## Slide 6
Potential map for each of four quad plates
bottom
inner
top
outer

## Slide 7
Tunes at Injection Tunes after ramp
Qx 0.9137 0.9039
Qy 0.4090 0.4403
Closed orbit, tunes, and b at injection and after ramp
Closed orbit after ramp at 0
 | Top | Bottom | Inner | Outer
Q1 | 32 | 22.7 | -32 | -32
Q2 | 32 | 22.7 | -22.7 | -32
Q3 | 32 | 22.7 | -32 | -32
Q4 | 32 | 22.7 | -32 | -22.7
Quad voltage at injection

## Slide 8
injection
E821 Quad voltage ramp
store

## Slide 9
At t=0, inject muons on displaced closed orbit.
Track 1000 turns
Quad plate voltage ramps as in E821
(Plot shows orbit at exit of Q4 on each turn)
Orbit shifted to center of aperture as quads ramp to nominal (symmetric voltage)
A small horizontal betatron oscillation is introduced by the ramp

## Slide 10
Simulation
70k muon distribution generated by Ditkys et. al.
Injected through hole in backleg iron, dipole fringe, inflector – includes scattering in inflector end coil. Wuzeng maps for Bfield
Kicker field based on field map. Amplitude tuned for optimum capture and minimum residual CBO.
Kicker temporal dependence as measured for prototype Blumlein kicker
Quadrupole E-field represented by maps generagted with FEMM. Nominal voltage ±32kV
Quad ramp as in NIM A503
45mm collimators as per doc db 3824

## Slide 11
With scraping
Muon distributions after 300 turns
Without scraping
2357/70000 (3.4%) stored
2153/70000 (3.1%) stored

## Slide 12
With scraping
No scraping
Transverse distributions after 300 turns
2153/70000 (3.1%) stored
2357/70000 (3.4%) stored

## Slide 13
Motion of centroid of muon distribution

## Slide 14
Evolution of width of muon distribution