## Slide 1: Test of Optical Stochastic Cooling in CESR
September 1, 2017

## Slide 2
kicker
pickup
bypass
amplifier
L3
Q48W
Q48E
9cm
DS = 2mm
beam

## Slide 5: Undulator
B0 = 750 G
lu = 0.4 m
K = 2.8
E = 0.5 GeV => g = 1000 => l = 1 mm
Example

## Slide 6
L3 bypass

## Slide 7
Delay bypass beam line
  Delay electron beam by about 2mm/c to compensate for time delay of optical amplifier and
  Couple transverse phase space to longitudinal position to enable cooling
  Tolerances consistent with optical wavelength (~1 micron)
Low energy (<0.5 GeV) operation of CESR
  Lattice design
  Injection
  Power supply stability, quads and dipole
  Undulators
  IBS
Demonstration of interaction of radiation from pickup undulator with radiation in kicker as a function of delay
  Detector?
Optics and optical amplifier amplifier
Demonstration of cooling
Components of OSC experiment

## Slide 8
What is the optical error tolerance of the delay bypass?
What are the alignment tolerances?
What is the intensity of the radiation for the relatively low bunch charge that we expect to circulate?
What is the optimal wavelength for the optical radiation?
What is the optimal undulator magnetic field?
What kind of signal do we expect to see?
Is there sufficient mixing?
What is the optimal emittance, energy spread, bunch length?
Gradient undulator or dipole undulator?
It is essential that we demonstrate the efficacy and tolerances of our design in simulation
=> Code for modeling radiation and absorption by electrons
Some questions that require new modeling tools

## Slide 9
CESR TA configuration

## Slide 10
L3 bypass

## Slide 11
CESR TA configuration

## Slide 12
Activity Start date
Lattice design 9/17
Bypass optics design - 10/17
Develop code and simulate cooling 60 days 10/17
Test of low energy operation of CESR 12/17
Bypass line magnet design - 1/18
Pickup/kicker undulator design 1/18
Bypass line vacuum component design 4/18
Second test of low energy operation 4/18
Bypass line engineering design - 6/18
Undulator engineering design 6/18
Undulator fabrication 10/18
Bypass line magnet fabrication 10/18
Bypass line vacuum fab 11/18
Fabricate support stands for bypass 1/19
Design optical amplifier 1/19
Test low energy optics in CHESS-U configuration 4/19
Design optical detector to measure interference 5/19
Installation of delay bypass 7/19
Commission bypass and demonstrate interference 12/19
Install optical amplifier and laser and detector 1/20
Demonstrate cooling (machine studies) 4/20
Schedule

## Slide 13
CHESS U 750 MeV
10 chess U undulators at 0.95T
750 MeV
Damping time 0.72 sec
Emittance 52 pm
V_RF=0.6MV => sigma_l=8.1mm

## Slide 14
CHESS U 750 MeV
10 chess U undulators at 0.45T
300 MeV
Damping time 8.3 sec
Emittance 6.5 pm
V_RF=0.6MV => sigma_l=2.2mm