## Slide 1: Test of Optical Stochastic Cooling in CESR
September 27, 2017

## Slide 2
Stochastic Cooling
Equilibrium emittance is a property of the storage ring magnet configuartion and beam energy
Stochastic cooling is a technique for reducing the emittance with a high bandwidth feedback system
  Damping rate scales with the bandwidth of the feedback
  SC proven effective with proton beams that have no radiation damping in the microwave regime (~ GHz– damping times measured in hours
Optical stochastic cooling is stochastic cooling with feedback that operates in the optical band (million GHz) – damping times < seconds - allowing promise for reducing emittance in electron beams
All feedback systems have:
  Pickup to measure the position or energy
  Kicker to correct the position and/or energy error
CESR multibunch feedback uses a BPM as pickup and a strip line kicker (100 MHz)
Optical stochastic cooling uses undulators for pickup and kicker

## Slide 3
Pickup measures offset
Kicker corrects offset
Multi bunch Feedback
Each represents centroid of distributon of particles

## Slide 4
Each bunch is a collection of particles
Goal: reduce bunch width (emittance)
=> cool the beam
Bunch width sx = 1
Bunch length = 10 mm

## Slide 5
0.1 mm slice of the distributioin

## Slide 6
Centroid of 0.1mm sllice

## Slide 10
Mixing as particles travel around the ring.
Now centroid of each slide is no longer at zero

## Slide 13
Pickup
Particles oscillate transversely in pickup undulator.
The wavelength of the radiation
E-field
k
E-field
k
amplifier

## Slide 15
L3 bypass
Tentative magnet plan
Replace Q49 with Q4W – (extended horizontal aperture) h = 9-20cm
CesrTA chicane magnets => 4 bends
4 new Panofsky style quadrupoles
2 new undulators – 6 pole, 1.5m, 500 G, normal conducting
Repurpose south arc choppers for Panofsky quads and undulators
Wide horizontal aperture vacuum chamber – new
(No change to Q48 E/W)

## Slide 16
Delay bypass beam line
  Delay electron beam by about 2mm/c to compensate for time delay of optical amplifier and
  Couple transverse phase space to longitudinal position to enable cooling
  Tolerances consistent with optical wavelength (~1 micron)
Low energy (<0.5 GeV) operation of CESR
  Lattice design
  Injection
  Power supply stability, quads and dipole
  Undulators
  IBS
Demonstration of interaction of radiation from pickup undulator with radiation in kicker as a function of delay
  Detector?
Optics and optical amplifier amplifier
Demonstration of cooling
Components of OSC experiment

## Slide 17
Delay bypass beam line
  Delay electron beam by about 2mm/c to compensate for time delay of optical amplifier and
  Couple transverse phase space to longitudinal position to enable cooling
  Tolerances consistent with optical wavelength (~1 micron)
Low energy (<0.5 GeV) operation of CESR
  Lattice design
  Injection
  Power supply stability, quads and dipole
  Undulators
  IBS
Demonstration of interaction of radiation from pickup undulator with radiation in kicker as a function of delay
  Detector?
Optics and optical amplifier amplifier
Demonstration of cooling
Components of OSC experiment

## Slide 18
kicker
pickup
bypass
amplifier
L3
Q48W
Q48E
9cm
DS = 2mm
beam