## Slide 1: Karnaugh maps
February 2, 2004
CS 231
<number>
Last time we saw applications of Boolean logic to circuit design.
  The basic Boolean operations are AND, OR and NOT.
  These operations can be combined to form complex expressions, which can also be directly translated into a hardware circuit.
  Boolean algebra helps us simplify expressions and circuits.
Today we’ll look at a graphical technique for simplifying an expression into a minimal sum of products (MSP) form:
  There are a minimal number of product terms in the expression.
  Each term has a minimal number of literals.
Circuit-wise, this leads to a minimal two-level implementation.

## Slide 2: Review: Standard forms of expressions
February 2, 2004
CS 231
<number>
We can write expressions in many ways, but some ways are more useful than others
A sum of products (SOP) expression contains:
  Only OR (sum) operations at the “outermost” level
  Each term that is summed must be a product of literals
The advantage is that any sum of products expression can be implemented using a two-level circuit
  literals and their complements at the “0th” level
  AND gates at the first level
  a single OR gate at the second level
This diagram uses some shorthands…
  NOT gates are implicit
  literals are reused
  this is not okay in LogicWorks!
f(x,y,z) = y’ + x’yz’ + xz

## Slide 3: Terminology: Minterms
February 2, 2004
CS 231
<number>
A minterm is a special product of literals, in which each input variable appears exactly once.
A function with n variables has 2n minterms (since each variable can appear complemented or not)
A three-variable function, such as f(x,y,z), has 23 = 8 minterms:
Each minterm is true for exactly one combination of inputs:
x’y’z’ x’y’z x’yz’ x’yz
xy’z’ xy’z xyz’ xyz
Minterm Is true when… Shorthand
x’y’z’ x=0, y=0, z=0 m0
x’y’z x=0, y=0, z=1 m1
x’yz’ x=0, y=1, z=0 m2
x’yz x=0, y=1, z=1 m3
xy’z’ x=1, y=0, z=0 m4
xy’z x=1, y=0, z=1 m5
xyz’ x=1, y=1, z=0 m6
xyz x=1, y=1, z=1 m7

## Slide 4: Terminology: Sum of minterms form
February 2, 2004
CS 231
<number>
Every function can be written as a sum of minterms, which is a special kind of sum of products form
The sum of minterms form for any function is unique
If you have a truth table for a function, you can write a sum of minterms expression just by picking out the rows of the table where the function output is 1.
f = x’y’z’ + x’y’z + x’yz’ + x’yz + xyz’
= m0 + m1 + m2 + m3 + m6
= m(0,1,2,3,6)
f’ = xy’z’ + xy’z + xyz
= m4 + m5 + m7
= m(4,5,7)
f’ contains all the minterms not in f

## Slide 5: Re-arranging the truth table
February 2, 2004
CS 231
<number>
A two-variable function has four possible minterms. We can re-arrange these minterms into a Karnaugh map.
Now we can easily see which minterms contain common literals.
  Minterms on the left and right sides contain y’ and y respectively.
  Minterms in the top and bottom rows contain x’ and x respectively.

## Slide 6: Karnaugh map simplifications
February 2, 2004
CS 231
<number>
Imagine a two-variable sum of minterms:
x’y’ + x’y
Both of these minterms appear in the top row of a Karnaugh map, which means that they both contain the literal x’.
What happens if you simplify this expression using Boolean algebra?
x’y’ + x’y = x’(y’ + y) [ Distributive ]
= x’  1 [ y + y’ = 1 ]
= x’ [ x  1 = x ]

## Slide 7: More two-variable examples
February 2, 2004
CS 231
<number>
Another example expression is x’y + xy.
  Both minterms appear in the right side, where y is uncomplemented.
  Thus, we can reduce x’y + xy to just y.
How about x’y’ + x’y + xy?
  We have x’y’ + x’y in the top row, corresponding to x’.
  There’s also x’y + xy in the right side, corresponding to y.
  This whole expression can be reduced to x’ + y.

## Slide 8: A three-variable Karnaugh map
February 2, 2004
CS 231
<number>
For a three-variable expression with inputs x, y, z, the arrangement of minterms is more tricky:
Another way to label the K-map (use whichever you like):

## Slide 9: Why the funny ordering?
February 2, 2004
CS 231
<number>
With this ordering, any group of 2, 4 or 8 adjacent squares on the map contains common literals that can be factored out.
“Adjacency” includes wrapping around the left and right sides:
We’ll use this property of adjacent squares to do our simplifications.
x’y’z + x’yz
= x’z(y’ + y)
= x’z  1
= x’z
  x’y’z’ + xy’z’ + x’yz’ + xyz’
  = z’(x’y’ + xy’ + x’y + xy)
  = z’(y’(x’ + x) + y(x’ + x))
  = z’(y’+y)
  = z’

## Slide 10: Example K-map simplification
February 2, 2004
CS 231
<number>
Let’s consider simplifying f(x,y,z) = xy + y’z + xz.
First, you should convert the expression into a sum of minterms form, if it’s not already.
  The easiest way to do this is to make a truth table for the function, and then read off the minterms.
  You can either write out the literals or use the minterm shorthand.
Here is the truth table and sum of minterms for our example:
f(x,y,z) = x’y’z + xy’z + xyz’ + xyz
= m1 + m5 + m6 + m7

## Slide 11: Unsimplifying expressions
February 2, 2004
CS 231
<number>
You can also convert the expression to a sum of minterms with Boolean algebra.
  Apply the distributive law in reverse to add in missing variables.
  Very few people actually do this, but it’s occasionally useful.
In both cases, we’re actually “unsimplifying” our example expression.
  The resulting expression is larger than the original one!
  But having all the individual minterms makes it easy to combine them together with the K-map.
xy + y’z + xz = (xy  1) + (y’z  1) + (xz  1)
= (xy  (z’ + z)) + (y’z  (x’ + x)) + (xz  (y’ + y))
= (xyz’ + xyz) + (x’y’z + xy’z) + (xy’z + xyz)
= xyz’ + xyz + x’y’z + xy’z

## Slide 12: Making the example K-map
February 2, 2004
CS 231
<number>
Next up is drawing and filling in the K-map.
  Put 1s in the map for each minterm, and 0s in the other squares.
  You can use either the minterm products or the shorthand to show you where the 1s and 0s belong.
In our example, we can write f(x,y,z) in two equivalent ways.
In either case, the resulting K-map is shown below.
f(x,y,z) = x’y’z + xy’z + xyz’ + xyz
f(x,y,z) = m1 + m5 + m6 + m7

## Slide 13: K-maps from truth tables
February 2, 2004
CS 231
<number>
You can also fill in the K-map directly from a truth table.
  The output in row i of the table goes into square mi of the K-map.
  Remember that the rightmost columns of the K-map are “switched.”

## Slide 14: Grouping the minterms together
February 2, 2004
CS 231
<number>
The most difficult step is grouping together all the 1s in the K-map.
  Make rectangles around groups of one, two, four or eight 1s.
  All of the 1s in the map should be included in at least one rectangle.
  Do not include any of the 0s.
Each group corresponds to one product term. For the simplest result:
  Make as few rectangles as possible, to minimize the number of products in the final expression.
  Make each rectangle as large as possible, to minimize the number of literals in each term.
  It’s all right for rectangles to overlap, if that makes them larger.

## Slide 15: Reading the MSP from the K-map
February 2, 2004
CS 231
<number>
Finally, you can find the MSP.
  Each rectangle corresponds to one product term.
  The product is determined by finding the common literals in that rectangle.
For our example, we find that xy + y’z + xz = y’z + xy. (This is one of the additional algebraic laws from last time.)

## Slide 16: Practice K-map 1
February 2, 2004
CS 231
<number>
Simplify the sum of minterms m1 + m3 + m5 + m6.

## Slide 17: Solutions for practice K-map 1
February 2, 2004
CS 231
<number>
Here is the filled in K-map, with all groups shown.
  The magenta and green groups overlap, which makes each of them as large as possible.
  Minterm m6 is in a group all by its lonesome.
The final MSP here is x’z + y’z + xyz’.

## Slide 18: Four-variable K-maps
February 2, 2004
CS 231
<number>
We can do four-variable expressions too!
  The minterms in the third and fourth columns, and in the third and fourth rows, are switched around.
  Again, this ensures that adjacent squares have common literals.
Grouping minterms is similar to the three-variable case, but:
  You can have rectangular groups of 1, 2, 4, 8 or 16 minterms.
  You can wrap around all four sides.

## Slide 19: Example: Simplify m0+m2+m5+m8+m10+m13
February 2, 2004
CS 231
<number>
The expression is already a sum of minterms, so here’s the K-map:
We can make the following groups, resulting in the MSP x’z’ + xy’z.

## Slide 20: K-maps can be tricky!
February 2, 2004
CS 231
<number>
There may not necessarily be a unique MSP. The K-map below yields two valid and equivalent MSPs, because there are two possible ways to include minterm m7.
Remember that overlapping groups is possible, as shown above.
y’z + yz’ + xy
y’z + yz’ + xz