## Slide 1: Digital Logic Families
PHYS3360/AEP3630
Lecture 26
<number>

## Slide 2: Overview
Integration, Moore’s law
Early families (DL, RTL)
TTL
Evolution of TTL family
ECL
CMOS family and its evolution
Overview
<number>

## Slide 3: Integration Levels
Gate/transistor ratio is roughly 1/10
  SSI < 12 gates/chip
  MSI < 100 gates/chip
  LSI …1K gates/chip
  VLSI …10K gates/chip
  ULSI …100K gates/chip
  GSI …1Meg gates/chip
<number>

## Slide 4: Moore’s law
A prediction made by Moore (a co-founder of Intel) in 1965: “… a number of transistors to double every 2 years.”
<number>

## Slide 5: In the beginning…
Diode Logic (DL)
simplest; does not scale
NOT not possible (need an active element)
=
=
Resistor-Transistor Logic (RTL)
replace diode switch with a transistor switch
can be cascaded
large power draw
<number>
Notes: <number>
RTL had economic advantage in that very few transistors were used. It was important when transistors were expensive to make (more expensive than resistors). Such times have long past.

## Slide 6: was…
=
Diode-Transistor Logic (DTL)
essentially diode logic with transistor amplification
reduced power consumption
faster than RTL
DL AND gate
Saturating inverter
<number>
Notes: <number>
RTL had economic advantage in that very few transistors were used. It was important when transistors were expensive to make (more expensive than resistors). Such times have long past.

## Slide 7: Logic families: V levels
VOH(min) – The minimum voltage level at an output in the logical “1” state under defined load conditions
VOL(max) – The maximum voltage level at an output in the logical “0” state under defined load conditions
VIH(min) – The minimum voltage required at an input to be recognized as “1” logical state
VIL(max) – The maximum voltage required at an input that still will be recognized as “0” logical state
VOH
VIH
VOL
VIL
<number>
Notes: <number>
These are: high-level output voltage (OH), low-level output voltage (OL), high-level input voltage (IH), low-level input voltage (IL)

## Slide 8: Logic families: I requirements
IOH – Current flowing into an output in the logical “1” state under specified load conditions
IOL – Current flowing into an output in the logical “0” state under specified load conditions
IIH – Current flowing into an input when a specified HI level is applied to that input
IIL – Current flowing into an input when a specified LO level is applied to that input
VOH
VIH
VOL
VIL
IOH
IIH
IOL
IIL
<number>
Notes: <number>

## Slide 9: Logic families: fanout
Fanout: the maximum number of logic inputs (of the same logic family) that an output can drive reliably
DC fanout = min( )
<number>
Notes: <number>

## Slide 10: Logic families: propagation delay
TPD,HL
TPD,LH
TPD,HL – input-to-output propagation delay from HI to LO output
TPD,LH – input-to-output propagation delay from LO to HI output
Speed-power product: TPD Pavg
<number>
Notes: <number>

## Slide 11: Logic families: noise margin
VNH
VNL
HI state noise margin:
VNH = VOH(min) – VIH(min)
LO state noise margin:
VNL = VIL(max) – VOL(max)
Noise margin:
VN = min(VNH,VNL)
<number>
Notes: <number>

## Slide 12: TTL
2-input NAND
Bipolar Transistor-Transistor Logic (TTL)
first introduced by in 1964 (Texas Instruments)
TTL has shaped digital technology in many ways
Standard TTL family (e.g. 7400) is obsolete
Newer TTL families still used (e.g. 74ALS00)
Distinct features
Multi-emitter transistors
Totem-pole transistor arrangement
Open LTspice example: TTL NAND…
<number>
Notes: <number>

## Slide 13: TTL evolution
Schottky series (74LS00) TTL
A major slowdown factor in BJTs is due to transistors going in/out of saturation
Shottky diode has a lower forward bias (0.25V)
When BC junction would become forward biased, the Schottky diode bypasses the current preventing the transistor from going into saturation
<number>
Notes: <number>
These also have lower power requirements than the standard TTL

## Slide 14: TTL family evolution
Legacy: don’t use in new designs
Widely used today
<number>
Notes: <number>
These also have lower power requirements than the standard TTL

## Slide 15: ECL
Emitter-Coupled Logic (ECL)
PROS: Fastest logic family available (~1ns)
CONS: low noise margin and high power dissipation
Operated in emitter coupled geometry (recall differential amplifier or emitter-follower), transistors are biased and operate near their Q-point (never near saturation!)
Logic levels. “0”: –1.7V. “1”: –0.8V
Such strange logic levels require extra effort when interfacing to TTL/CMOS logic families.
Open LTspice example: ECL inverter…
<number>
Notes: <number>
These also have lower power requirements than the standard TTL

## Slide 16: CMOS
Complimentary MOS (CMOS)
Other variants: NMOS, PMOS (obsolete)
Very low static power consumption
Scaling capabilities (large integration all MOS)
Full swing: rail-to-rail output
Things to watch out for:
  don’t leave inputs floating (in TTL these will float to HI, in CMOS you get undefined behaviour)
  susceptible to electrostatic damage (finger of death)
Open LTspice example: CMOS NOT and NAND…
<number>
Notes: <number>
These also have lower power requirements than the standard TTL

## Slide 17: CMOS/TTL power requirements
TTL power essentially constant (no frequency dependence)
CMOS power scales as  f  C  V2
At high frequencies (>> MHz) CMOS dissipates more power than TTL
Overall advantage is still for CMOS even for very fast chips – only a relatively small portion of complicated circuitry operates at highest frequencies
frequency
supply volt.
eff. capacitance
<number>
Notes: <number>
These also have lower power requirements than the standard TTL

## Slide 18: CMOS family evolution
obsolete
Reduction of dynamic losses through successively decreasing supply voltages: 12V 5V 3.3V 2.5V 1.8V
CD4000 LVC/ALVC/AVC
Power reduction is one of the keys to progressive growth of integration
General trend:
<number>
Notes: <number>
These also have lower power requirements than the standard TTL

## Slide 19: Overview
TTL
Logic
Family
CMOS
Values typical for Vcc/Vdd = 5V
When interfacing different families, pay attention to their input/output voltage, current (fanout) specs.
TPD Trise/fall VIH,min VIL,max VOH,min VOL,max
Noise
Margin
<number>
Notes: <number>
These also have lower power requirements than the standard TTL

## Slide 20: Life-cycle
<number>
Notes: <number>
These also have lower power requirements than the standard TTL